## Slide 1
Human error and system failure
Notes: Welcome to Module 1, Snippet 3 of Safe System for Universities. In Snippet 2, we discussed mechanisms of failure, including one type of latent condition that can lead to error, known as error provoking conditions. In this snippet, we will look closer at error and the role it plays within system failures.

## Slide 2
1.1
01 Jul 2020
Press enter to continue

## Slide 3: About this snippet
This snippet is made up of a number of sections. Click on the below links to go through each section. To advance a slide, press enter on your keyboard or click the slide.
Go to What is error?
Start here
Go to Failure trajectory
Go to Kimber’s model
Go to Example: Piper Alpha
Notes: This snippet is made up of a number of sections. Click on the below links to go through each section. To advance a slide, press enter on your keyboard or click the slide. If you miss anything that has been said, you can replay the narration to each slide. A printed version of the narrative is also provided in the curriculum guideline.

## Slide 4
What is error?
Notes: Firstly, let’s revisit errors and their effect.

## Slide 5: Latent conditions and error
Latent conditions that lead to error
Most errors do not result in loss…
…but some ultimately lead to harm
Source: This Photo by Unknown Author is licensed under CC BY
Source: This Photo by Unknown Author is licensed under CC BY-SA-NC
Press enter to continue
Notes: Errors occur when latent conditions provoke erroneous decisions made by system managers and system users. The latent condition that leads to errors is known as an error provoking condition. Error provoking conditions can take many forms and may not always be obvious, as we may consider them a part of normal operating conditions. Two examples are the time pressures placed on engineers when completing a design, and the necessity for drivers to pick a gap in traffic in order to turn at an intersection.
Errors do not always lead to harm. Most errors will result in no-loss failures, which are failures that do not result in property or injury loss to those involved. These types of failures are referred to as near misses, incidents and no-incident failures. Some no loss failures such as near misses, are easily recognisable. Others, such as non-incident failures, can easily go unnoticed.
Some errors will lead to harmful failures, which are commonly referred to as accidents. Harmful failures lead to some form of loss to those involved, whether it be loss of property, injury or loss of life. As with no-loss failures, the errors that lead to these events may be intentional or unintentional.

## Slide 6: Types of error
Latent or active
Latent errors made by system managers
Active errors made by system users
Source: This Photo by Unknown Author is licensed under CC BY-NC-ND
Source: Centre for Automotive Safety Research
Press enter to continue
Notes: Errors can be either latent or active.
Latent error refers to errors that cause latent conditions within a system. They are usually due to decisions made by system managers, such as planners, designers and operations managers. Examples could be inadequate design, inappropriate procedures, understaffing and hazardous operating conditions.
Active errors are those made directly before a failure occurs. Active errors are usually made by system users, such as front line workers and the public. Examples of active errors could be a pilot undertaking a hazardous manoeuvre, a machine operator activating the wrong control, or a pedestrian crossing the road when traffic is present.

## Slide 7
Failure trajectory
Notes: Failure trajectory refers to the chain of conditions that lead to a failure. In this section, we will look at a well known model of failure trajectory.

## Slide 8: Swiss cheese model
James Reason’s model of failure trajectory
Window of opportunity for failure to occur
Takes only one barrier to prevent failure
Barriers to failure
Failure trajectory
Failure
Source: Based on Reason (1990)
Press enter to continue
Notes: James Reason’s swiss cheese model is a well known example of failure trajectory. In it, barriers to failure are represented as layers through which the failure trajectory must navigate.
Holes in these layers, which represent latent conditions and subsequent errors, must align in the right place and at the right time for a failure to occur. In other words, a window of opportunity forms through which the failure trajectory can traverse.
When the holes in the layers do not align, the failure cannot occur. Much like a person walking through a succession of doors to reach a destination, it only takes one locked door in order to prevent the person from reaching their destination. Like this analogy, it only takes one layer to form a barrier for failure to be prevented.
It is important to note that holes within one layer can circumvent the effects of other layers. For example, policy implemented by system decision makers may be weakened if it is not implemented properly by line management, or followed by system users.

## Slide 9: Swiss cheese model
System decision makers
Preconditions
Defences
Line management
Productive activities
Source: Based on Reason (1990)
Press enter to continue
Notes: Each layer represents a different level of activity where barriers are created and where failures can occur.
The first layer represents the objectives and strategic directions that decision makers will choose to follow. An example can be the directions made by an organisation within their strategic planning.
The second layer represents line management, which is responsible for implementing system functions. An example of line management can be the introduction of new policies in the operation of a manufacturing plant.
The third layer represents the preconditions that exist within a system. Preconditions can be the use of appropriate and reliable equipment, the availability of appropriate design and operation conditions, and the undertaking of system use by skilled and compliant users. An example can be the type of controls used at intersections along a roadway.
The fourth layer represents productive activities, the actual performance of equipment and users who undertake tasks within a system. Examples of productive activities can be the performance of pilots flying an aircraft, of workers using construction machinery, or of a reactor core used in the production of electricity at a nuclear power plant.
The last layer to failure represents the defences that safeguard from failure. Examples of defences include the use of driver assistance technology in vehicles or the autopilot systems used in aircraft. Examples can also include failsafe and emergency shutdown mechanisms employed on equipment and machinery, and physical barriers used to separate workers from large vehicles at mine sites.

## Slide 10: Swiss cheese model of harm
Model transformed to show trajectory to harm
Layers also affect consequence of failure
Harm prevented by eliminating failure or reducing consequence
Likelihood
Likelihood
Likelihood
Likelihood
Likelihood
Consequence
Consequence
Consequence
Consequence
Consequence
Source: Based on Reason (1990)
Press enter to continue
Notes: While the swiss cheese model as developed by Reason gives us a good understanding of the trajectory to failure, its focus is aligned only towards the likelihood of failure and not its consequences.
If we introduce consideration of the consequences of failure in addition to factors that affect likelihood, we can transform the model to that which represents a trajectory to harm.
Consequence, here represented by the size of the holes in each layer, dictates the magnitude of harm when failure occurs. Each layer has the ability to affect the magnitude of harm.
We can see that there are now two ways in which harm can be prevented. Each layer can form a barrier to prevent failure from occurring, by removing the latent conditions and subsequent errors from the failure trajectory. In this scenario, the barriers have worked to prevent failure from occurring in the first place.
But we also know that failure cannot be prevented 100% of the time. The second way harm can be prevented is by using each layer to reduce the magnitude of consequence. While latent conditions and their subsequent errors are allowed to occur, actions undertaken within each layer affect the magnitude of harm. Used appropriately, each layer has the opportunity to reduce the magnitude of harm to a point where the failure may occur, but harm is avoided.

## Slide 11
Kimber’s model
Notes: Now, we will take a look at Kimber’s model, which helps highlight two very different ways of perceiving failure. It is important to note that this model was developed specifically as a way to represent failure in the road transportation industry.

## Slide 12: Kimber’s model
Modes of failure leading to crashes
Represents three common factors
Modified to show magnitude of contribution
Source: Based on Kimber (2005)
Driver
Vehicle
Road
Press enter to continue
Notes: Kimber’s model is used to describe the relative contributions of different factors in the causation of road crashes. The model is shown as a Venn diagram of failure modes in which a single factor is deemed responsible, as represented by the non-overlapping areas of the circles, and of failure modes in which more than one factor is deemed responsible, as represented by the overlapping portions of the circles.
As shown here, the model represents three factors commonly associated with road crashes. These are the driver that is in control of a vehicle, the road environment on which a vehicle is being driven, which includes the speed limit along the road, and the vehicle that is being driven. This model as we see it here identifies the relationships between the different factors, but does not attribute the magnitude of contribution by each factor.
If we consider the relative contribution of each factor, we can see that driver error contributes to most crashes, while road and vehicle failures, such as reduced pavement friction or defective brakes, contribute to a lesser proportion of crashes. In this sense, the model is correct, but of what use? In short, its use is limited when an important omission within this model is considered. This model give no consideration to error provoking conditions, which ultimately lead road users to make the errors that contribute to most crashes.

## Slide 13: Kimber’s model
System failures rather than user error
Considers all contributing factors
Applicable to other industries
Source: Based on Kimber (2005)
System failures
(driver / vehicle / road)
Driver failure: Excess
Driver failure: Inexperience
Press enter to continue
Notes: A more appropriate model is that of Kimber’s revised model, which draws a perspective on system failures, rather than isolating human error. In this form of the model, we can also appreciate the contributions of error provoking conditions. Seen through this perspective, we can now see that system failures, which stem from both system deficiencies and error provoking conditions, are responsible for the vast majority of crashes. Human error in isolation is responsible for only a small number of crashes, which generally involve either extreme non-compliance or inexperience.
We can now see that system failures, as shown here, represent the multitude of latent conditions and active errors that lead to a crash. The benefit of this perspective is to take focus away from just the contribution of error made by the driver. When we draw focus to the system perspective, we can see that driver error is just one link in a chain of actions that lead to a crash. Take any of these links away, and the crash would not occur in the first place. This then begs the question, is driver error really to blame when it was weaknesses within the system that allowed error to translate to a crash?
While Kimber’s model was created specifically to demonstrate the fallibility of focusing solely on human error in finding the causes for car crashes, it can be applied equally as well to many other industries. The point of the model is to demonstrate that the entire system, comprising latent conditions as well as active errors, contributes to failures. By looking at the entire system, instead of focusing on one small part of it, we are able to better understand the conditions that lead to failures and employ more diverse solutions for mitigating their damaging results.

## Slide 14
Example: Piper Alpha
Notes: On 6 July 1988, a drilling platform in the North Sea, about 190 kilometres north-east of Aberdeen in Scotland, was engulfed in a series of explosions that ultimately destroyed the platform and cost the lives of 167 people. This platform, named Piper Alpha, is a prime example of the intrinsic relationships that occur between human errors and system failures. As with many disasters, it is easy to pinpoint the failures on Piper Alpha to the mistakes made by the work crew operating the system. On the surface, these mistakes may appear to carry the bulk of responsibility for what occurred. But when we look a little deeper, the failures that occurred within the system, some lying unnoticed for many years, ensured that the mistakes that occurred on 6 July 1988 resulted in such a catastrophic outcome.

## Slide 15: Piper Alpha
Source: This Photo by Unknown Author is licensed under CC BY-NC
System decision makers
Defences
Line management
Productive activities
Preconditions
Used as central transfer point
Production continued during upgrade work
Less separation from hazards
Overhauled Pump A not isolated
Handover not completed
Pump B failed to restart
Firefighting pumps in manual mode
Reverted to using Pump A
Firewall failed in explosion
No chain of command
No firefighting equipment
Personnel quarters collapsed
Press enter to continue
Notes: Using Reason’s swiss cheese model, we will attempt to reconstruct the failure that occurred on Piper Alpha. While this will not be an exhaustive reconstruction, it will enable us to visualise, from a system’s perspective, some of the latent conditions and errors that led to the disaster.
Piper Alpha was constructed in the early 1970s and began oil production in 1976. The platform was chosen to act as a central transfer point for production, with nearby drilling platforms transferring production to Piper Alpha before being piped to the mainland. This decision would play a critical role in the disaster.
For safety reasons, personnel areas were kept well away from the most hazardous areas of production. In 1980, the platform was converted to allow gas production in addition to oil. With this conversion, a number of hazardous operations were brought closer to crew areas, including locating the gas conservation module near the crew’s accommodation quarters.
In the late 1980s, upgrade and reconstruction work to the platform had begun. Part of this work called for upgrade of a gas conservation module, or CGM. While the CGM was being upgraded, the decision was made to continue oil production and transfer of gas from the other drilling platforms, instead of ceasing production altogether.
Part of the upgrade works occurring at the time required divers to be in the water under the platform. Procedure called for the normally automatically controlled firefighting pumps to be placed in manual mode whenever divers were working. After the first explosion, system controls were destroyed to the extent where the firefighting equipment could not be manually started.
On 6 July, 1988, Pump A of two condensate pumps was scheduled for routine maintenance. These pumps were used for removing condensate from gas being transferred from the other platforms, before it was piped to the mainland. The pump’s pressure safety valve was removed during this work. Because the maintenance could not be completed before shift change over, a temporary cover plate was used to seal the pump’s open pipework. Because it was meant to be temporary, the plate was only hand-fastened.
When the shift change over occurred, the maintenance engineer filled in the appropriate paperwork notifying that Pump A was offline and not to be started. Because he could not speak to the oncoming shift controller, the engineer did not inform him of the situation. While the paperwork was completed, it was stored in a different location to the original maintenance work permit form and was never found by the oncoming crew.
At some point, Pump B, which had being taking the entire condensation load, failed and was not able to be restarted.
As the on-duty crew was not aware of Pump A’s condition, it was started. The temporary cover plate failed to hold and gas started to escape from the pipe. The gas ignited and exploded.
The firewall designed to isolate the condensate pump was not designed to withstand such an explosion and so it failed, leaving the nearby control room to be destroyed and disabling several critical control systems.
Without the control room, the platform’s chain of command soon collapsed and proper emergency procedures failed to be actioned. Upon learning of the explosion, the majority of the platform’s crew escaped to the fireproof accommodation quarters.
The firefighting equipment was still in manual mode. The equipment’s manual control systems were damaged during the initial explosion, ensuring the platform’s own firefighting equipment would not start. Even if it had been started, Piper Alpha was transferring gas and oil from nearby platforms. Due to company pressure to maintain production, the crews of these platforms had not shut down production upon hearing of the emergency. Despite Piper Alpha’s own production being stopped, gas was still flowing at a rate that made the fire virtually unstoppable.
Due the intensity of the fire and subsequent explosions, the platform’s structure nearest to the initial explosion started to disintegrate. The accommodation quarters were one of the initial structures that collapsed and fell into the sea, resulting in the deaths of all who were sheltering inside.

## Slide 16: Piper Alpha
What errors led to the disaster?
How could a system’s focus help?
System wide response
Source: This Photo by Unknown Author is licensed under CC BY-NC
Press enter to continue
Notes: While it is easy to point to the crew’s communication mistakes for the disaster, Reason’s swiss cheese model helps us to visualise the wider scope of holes that formed in each barrier along the trajectory to failure.
We must therefore ask ourselves, does it help to focus our attention on the errors made by the crew? Would it help to take a broader perspective of the events that led to the disaster? Hopefully, you can see how a system wide focus can help understand all of the events that led to failure.
In taking a system wide focus, we also enable ourselves to see the wider scope of responses that could have prevented such a disaster from occurring, or at least lessened the magnitude of the harm that it caused. This is the real power of viewing failure as a system wide problem, rather than a result of only user error.