## Slide 1
Managing risk
Notes: Welcome to Module 1, Snippet 4 of Safe System for Universities. In this Snippet, we will take a look at the different ways in which risk is managed within industry.

## Slide 2
1.1
01 Jul 2020
Press enter to continue

## Slide 3: About this snippet
This snippet is made up of a number of sections. Click on the below links to go through each section. To advance a slide, press enter on your keyboard or click the slide.
Go to Risk management approaches
Start here
Go to M&R industry approach
Go to Aviation approach
Go to Road transport approach
Notes: This snippet is made up of a number of sections. Click on the below links to go through each section. To advance a slide, press enter on your keyboard or click the slide. If you miss anything that has been said, you can replay the narration to each slide. A printed version of the narrative is also provided in the curriculum guideline.

## Slide 4
Risk management approaches
Notes: In this first section, we will take a look at the general considerations required when considering the suitability of risk management approaches.

## Slide 5: Finding the right approach
How much control do I have?
High control of trained workforce
Low control over general public
Source: This Photo by Unknown Author is licensed under CC BY
Source: This Photo by Unknown Author is licensed under CC BY-SA
Press enter to continue
Notes: The way we manage the risk of harm really depends on the system in which the harm can occur. While there are likely many factors that need to be considered, one important factor is the level of control that system managers possess over the system.
The amount of control that system managers possess is largely dependent on their control over people operating within the system. In highly controlled environments referred to as closed systems, like a mine site or a nuclear power facility, strict control is maintained over those working within the system. Access to potentially hazardous locations or tasks is strictly limited to need and the performance of users can be maintained at a very high level through training and procedure.
At the opposite end of the scale, low control environments referred to as open systems are those where public access is largely unlimited and access conditions are minimal. The road transport system is a prime example. While a driver’s license is required for using a motor vehicle, this provides a very low threshold of training. Other access conditions, such as for pedestrians, are uncontrolled. With such little control over access to the system, it is virtually impossible to ensure any level of performance of those operating within the system.

## Slide 6: Finding the right approach
What’s the consequence?
How effective is mitigation?
Source: This Photo by Unknown Author is licensed under CC BY
Press enter to continue
Notes: Another important factor is the consequence of harm, should it be allowed to occur. This not only refers to the severity of harm that may be experienced by an individual, but also the scale of harm that could occur. A good example is fire control in buildings. While building fires come with the potential for severe consequences any context, high occupancy buildings such as apartment towers are especially concerning given the number of people that may be effected by a single failure.
While consequence may be severe, the response to it will depend on how effective are the mitigation strategies able to be employed. In some contexts, mitigation may be a feasible approach and so a focus on reducing the consequence of failure is beneficial. Sometimes, the consequence of failure is likely to be so intolerable or the effects of mitigation strategies so ineffective that allowing any failure to occur is unacceptable. The nuclear power industry is a prime example of such a situation. Because of this, the main focus in this industry is eliminating the likelihood of any failures that involve the release of radioactive material, which is the prime danger presented by the industry.

## Slide 7
M&R industry approach
Notes: Now, let’s consider the case of a widely known approach to safety management, that utilised by the manufacturing and resources industries.

## Slide 8: M&R industry approach
Broad range of activities
Widely employs Hierarchy of Controls
Substantial control over access
Source: This Photo by Unknown Author is licensed under CC BY-NC-ND
PPE
Administrative controls
Engineering controls
Substitution
Elimination
Press enter to continue
Notes: When we think of the word industry, the manufacturing and resources industry is front of mind for many people. This industry employs a substantial proportion of people in Australia and New Zealand, incorporates a wide variety of activities, and sees a substantial amount of exchange within the workforce. Because of this, importance is placed on employing controls that can be widely understood and applicable at a general industry level.
The hierarchy of controls is a well known system that has become the benchmark for managing safety within the manufacturing and resources industry. The hierarchy is generally applied at an activity level of operation, such as a process for undertaking a specific task or the operation of a specific type of equipment. It provides guidance for the appropriate order in which controls should be considered, giving priority to categories of control that provide the most effective means for mitigating harm.
A key enabler of the hierarchy of control is the environment in which it is applied. The method of categorising and prioritising controls is well suited to systems where control over access and use is well established. The high level of system control by system managers, and the high level of access control and task specific training given to system users means that controls in each category can be strictly applied with minimal non-conformance. While the hierarchy of controls can be applied to systems with much less control over access and use, its effectiveness would be limited by the low level of control that could be utilised before non-conformance becomes a substantial issue.

## Slide 9: Hierarchy of Controls
PPE
Administrative controls
Engineering controls
Substitution
Elimination
Eliminating of the source of harm
Substituting the source of harm with something less harmful
Utilising infrastructure to protect people from the hazard
Limit exposure to the hazard
Personal protective equipment
Press enter to continue
Notes: At the top of the hierarchy of controls is elimination. Wherever possible, priority should be given to eliminating the source of harm. This could mean eliminating a non-essential activity, removing people from a task that can be automated, or removing people from an area where a hazardous task is being undertaken. A good example is the elimination of mining personnel from areas where heavy mining machinery is being operated.
If the source of harm cannot be eliminated, then it should be substituted with something less harmful. This could mean substituting with a less harmful task, process or product. Substitution is commonly used as a method for reducing the harm associated with consumer products, such as paints, pesticides, cleaning products and building materials. Substitution works well when the hazard being mitigated is not replaced with another hazard, such as producing a less hazardous product for end consumers that requires a more hazardous production method for those making the product.
If the hazard cannot be eliminated or substituted to the extent where a hazard no longer exists, then engineering controls can be employed to protect people from the effects of the hazard. Engineering controls generally take the form of barriers to separate people from the hazard, lockout and shutdown controls to contain a hazard, and ventilation systems to extract toxic substances before they become inhaled. Engineering controls could also take the form of ergonomic treatments to prevent injury through repetitive actions.
Administrative controls should be employed only when the hazard cannot be removed or people protected from the hazard. Administrative controls are used to alter the way in which people work within a hazardous activity. This could mean changing work procedures, undertaking training, placing warning signs or changing the time or location of an activity to one less hazardous, such as rescheduling outdoor work to cooler times of the day during summer.
PPE, or personal protective equipment, is used as a last line of defence when all other controls are inadequate to protect a person from harm. PPE is generally used to shield a person from a hazard, such as with the use of respirators and chemical gloves, to reduce the risk of harm from a hazard, such as through the use of hard hats, or to reduce the likelihood of error, such as by wearing high visibility clothing.

## Slide 10
Aviation approach
Notes: Next, we’ll take a look at safety management within the aviation industry.

## Slide 11: Aviation approach
Source: This Photo by Unknown Author is licensed under CC BY-SA
Source: This Photo by Unknown Author is licensed under CC BY-ND
Multi-factor approach
Shared responsibility
Investigation & action from incidents
Global approach
Press enter to continue
Notes: The aviation approach to managing risk, especially for the larger airline industry, has evolved into a system with a focus on eliminating failures that result in intolerable outcomes, and reducing the consequences of failures that may result in less catastrophic levels of harm.
Part of the success of safety within the aviation industry has been down to a culture of shared responsibility. Safety responses within the aviation industry are at a system level. This means that when a problem is identified, the entire industry responds.
Another part of the success of this approach has been through the investigation of no harm failures to better understand and develop controls against failures that do result in harm. Learnings from these investigations are critical to understanding the mechanisms of failure and implementing controls to mitigate their effects.
Success has also been established on global communication within the industry that helps maintain a level of consistency in the approach throughout the industry. This has been facilitated by the fact that the airline industry works across international boarders.

## Slide 12: Safety Management System
Latest safety management mechanism
Based on four pillars
Introduces a system approach
Safety policy
Safety assurance
Safety risk management
Safety promotion
Policy
SRM
SA
Promotion
Source: Federal Aviation Administration (accessed Oct 2019)
Press enter to continue
Notes: The latest safety management mechanism employed in the aviation industry is the Safety Management System, or SMS. This system marks a shift towards a systems based approach to safety, and away from the human error based approaches that were previously practiced.
The Safety Management System is based on four pillars. Safety policy establishes senior management’s commitment to safety. Safety risk management determines the need for and adequacy of risk controls, which safety assurance then evaluates the continued effectiveness of these controls. Finally, safety promotion creates a positive safety culture through training and communication.
SMS brings a systems approach to assess and control risks, while ensuring that controls remain adequate. Unlike previous generation safety systems such as Crew Resource Management, SMS is aimed all levels and areas of the aviation industry, rather than through a focus on front line employees alone.

## Slide 13
Road transport approach
Notes: Lastly, let’s look at a new way safety management is being approached in the road transport industry.

## Slide 14: Transformation to a Safe System
Low level of access control
Consequence focussed approach
Safe System
Source: Centre for Automotive Safety Research
Source: Centre for Automotive Safety Research
Press enter to continue
Notes: With regard to the management of safety, the road transportation industry is defined by its low level of access control. While licencing provides some measure of control for those using motor vehicles, all other access is largely uncontrolled. This makes any form of control over individual use of the system almost impossible. While previous efforts to curtail substantial non-compliance through education, training and enforcement have provided success, there is a growing understanding that any chance to eliminate severe harm will require an additional focus on consequence.
This focus on consequence has come from the understanding that, with such low levels of access control, system users will continue to make errors at a rate that means severe harm is a foreseeable and all too common event. In light of this, the approach to safety has been shifted to a systems based approach that prioritised the reduction of failure consequence.
This approach is the Safe System, which is based on the philosophy that people will continue to make errors, but that the road system should not allow these errors to translate to severe harm. Contrary to historical approaches that have focussed almost exclusively on reducing user error, the Safe System places the onus of eliminating severe harm on system managers.

## Slide 15: What is the Safe System?
Errors will occur but severe harm is avoidable
Commonly represented as four pillars
Responsibility led by system managers
Safe
roads
and roadsides
Safe
road users
Safe vehicles
Safe
speeds
Shared responsibility led by system managers
Press enter to continue
Notes: The Safe System is based on the fundamental understanding that system users will make mistakes. The philosophy behind the Safe System is that severe harm should not result as a consequence of these mistakes. To align with this philosophy, a systems based approach is used to focus on eliminating severe consequences while also reducing exposure and the likelihood of crashes.
The Safe System is often represented as four pillars, which refer to the need for safe roads and roadsides that are forgiving of error, safe road users that comply with system rules, safe vehicles that cushion crash forces, and safe speeds that ensure crash forces are not allowed to exceed the human body’s physical limits before severe harm occurs.
While the Safe System calls for a shared responsibility between system managers and system users, the onus is placed with system managers to ensure that severe harm does not occur. This means that when severe harm does occur within the system, it is the responsibility of system managers to take corrective action and control the level of harm that can possibly occur.