## Slide 1
Design that supports harm elimination
Notes: Welcome to Module 2, Snippet 6 of Safe System for Universities. In this snippet, we will look at the aspects of road design and operation that supports a Safe System. We will introduce some of the concepts that will feed into Module 3 of Safe System for Universities, where we will take a closer look at the practical design of safe roads.

## Slide 2
1.0
01 Jul 2020
Press enter to continue

## Slide 3: About this snippet
This snippet is made up of a number of sections. Click on the below links to go through each section. To advance a slide, press enter on your keyboard or click the slide.
Go to Achieving zero harm
Start here
Go to Design that supports harm elimination
Go to Harm elimination examples
Go to Identifying Safe System design
Notes: This snippet is made up of a number of sections. Click on the below links to go through each section. To advance a slide, press enter on your keyboard or click the slide. If you miss anything that has been said, you can replay the narration to each slide. A printed version of the narrative is also provided in the curriculum guideline.

## Slide 4
Achieving zero harm
Notes: Firstly, we will look at what it will take to achieve zero harm within our road transportation system.

## Slide 5: Elements of harm elimination
Remove risk of fatal and serious injury outcomes
E.g. Install flexible median and roadside barriers
E.g. Reduce speed limits near intersections
Remove exposure to crash potential
E.g. Reduce traffic volumes along a higher risk route
E.g. Remove or grade-separate an intersection
Shift exposure to a safer alternative
E.g. Promote use of higher ANCAP rated vehicles
E.g. Divert traffic to a safer part of the network
Reduce crash likelihood
E.g. sealed shoulders on rural roads
E.g. mandate vehicle stability control systems
Complete elimination of likelihood unlikely – need to consider severity
Exposure
Likelihood
Severity
Press enter to continue
Notes: The design and operation of our road transport system is a key element in the quest for eliminating fatal and serious injuries. Designing and operating the road transport system in a manner that supports harm elimination is a key responsibility of those who manage the system. Primarily, this will mean the direct design and operation of the road network. However, this can also mean decision making and influence in other sectors such as through the vehicle industry, where the implementation of vehicle safety technology has had a substantial influence on road safety. Design and operation that supports harm elimination can be categorised into three general elements. Certain design and operation may fall into one or more of these elements, and the definitions of each element can somewhat overlap. The importance of this categorisation is to help consider how harm elimination is affected and what is needed for it to be achieved.
The first element is exposure. This means removing people from situations where harm can occur. This can mean reducing absolute exposure, such as reducing the volume of traffic moving through an unprotected area of the road network, or by removing the need for higher risk activities. Grade separation is an obvious example, as it reduces exposure to intersection type interactions by removing the need for traffic streams to intersect. Exposure can also be relative, such as by increasing the relative proportion of the light vehicle traffic fleet that has a higher Ancap star rating.
The second element is likelihood. Historically, this has been the mainstay of most road safety activities. While a crucial part of road safety, like all elements it is important to recognise its place and limitation in the context of harm elimination. Reducing likelihood takes the form of design and operation that reduces the chances that road users will be involved in a crash. Road design that reduces likelihood can include such treatments as the sealing of shoulders on rural roads and the signalisation of intersections. Likelihood can also be affected outside of road design and operation, such as through mandating vehicle technology that reduces crash likelihood.
The third element of harm elimination is severity. Historically, our influence on crash severity has been limited. However, our ability to achieve harm elimination will be dependent on our ability to control crash outcomes. Reducing severity means reducing the impact of crashes on the human body to the extent where the human biomechanical tolerance to harm is not exceeded. This can mean reducing the energy of crashes, such as through lower speeds, using energy absorbing roadside safety barriers and removing non-frangible roadside objects. It can also mean reducing the transfer of energy to the human body, such as through the use of airbags and seatbelts in vehicles.

## Slide 6: Safe System treatment hierarchy
Supporting FSI outcomes are reduced
Supporting – step towards FSI outcomes are reduced; supports future implementation of primary treatments
Primary
Fatal and serious injury (FSI) outcomes for known crash mechanisms are virtually eliminated
Press enter to continue
Notes: As each treatment can affect a different element of harm elimination, the level to which each treatment can affect harm elimination can also be different. For this reason, road safety treatments are also categorised according to their ability to eliminate harm. Under the Safe System, these categories are known as primary, step-towards and supporting treatments. A further category, known as other considerations, are elements that lie outside of road network management, such as speed enforcement, or that have an indirect contribution to road safety, such as line marking consistent with autonomous vehicle technology. The Austroads Safe System Assessment Framework research report provides lists of primary, step-toward and supporting treatments for major crash types.
Primary treatments are named as such because they should be the primary consideration for road design and operation. Primary treatments are those that are known to produce near-fatal and serious injury elimination outcomes. While we must acknowledge that no road infrastructure treatment alone will achieve zero harm, the combination of primary treatments and actions within the other Safe System pillars represent our best opportunity to achieve zero harm. Most primary treatments achieve harm elimination through a reduction in crash severity, a reduction in exposure, or a combination or reduced severity and reduced likelihood. At this stage, few true primary treatments have been identified.
Supporting treatments are those that should be considered once the option for primary treatments has been exhausted. Step-toward treatments are the most desirable of the supporting treatments. They are so named because they provide a stepping stone towards the implementation of primary solutions and harm elimination, with minimal redundancy of investment. A classic example of a step-toward treatment is the use of wide centrelines along undivided rural roads, which provide enough space for flexible centreline barriers to be retrofitted at a later date.
Non-step-toward supporting treatments are those that support harm reduction but do not provide a direct pathway towards harm elimination. Because of their reduced ability to support harm elimination, these supporting treatments should only be considered when primary and step-toward solutions cannot be sought. Many supporting treatments work by limiting the likelihood of crashes, but do not deal with the severity of crashes when they occur. Some common examples of support treatments are full signalisation at intersections, rigid safety barriers, audio tactile line marking and sealed shoulders on rural roads, and speed reduction to non-Safe System speeds.

## Slide 7
Design that supports harm elimination
Notes: Now, let’s look at some concepts behind road design and operation that supports harm elimination.

## Slide 8: Design that supports harm elimination
Reduce crash energy by reducing speed
Reduce impact angles
Source: based on Austroads (2017)
Source: Transport Accident Commission of Victoria
U1
U2
Press enter to continue
Notes: Speed is a key decider in the ability for harm to occur. As speed increases, the likelihood of a crash occurring also increases, as does the severity of the crash when one occurs. Appropriate speed management is one of the most effective tools that we have for eliminating harm. Safe System speeds, which is a fancy term for speeds at which fatal and serious outcomes and very unlikely to occur, should guide road designers and operators in their decision making processes. While the exactness of these speeds is still widely debated, there is little objection that currently the majority of speed management and speed limits across our road network are well above what is deemed to be safe.
Beside speed, the impact angles between colliding vehicles is another important factor in determining crash severity. Head-on and right angle crashes are more likely to result in high severity outcomes that rear-end orientated collisions. This is because the relative speed of the colliding vehicles is much higher and, especially in the case of right angle crashes, the ability for the vehicle to protect its occupants is limited.

## Slide 9: Design that supports harm elimination
Reduce crash energy by reducing speed
Reduce impact angles
Forgiving roadside hazards
Source: Safe System Solutions
Source: Safe System Solutions
Press enter to continue
Notes: Along with other vehicles, roadsides are one of the most hazardous aspects of the road transportation system. This is because vehicles can depart the roadway and collide into hazardous objects. It is highly preferable that any roadside objects able to be reached by errant vehicles be made frangible. This means that they will bend or break on impact with very little force on the colliding vehicle. Of course, this is not always possible and, as will be discussed in the next module, vehicles are able to reach object located a surprisingly far distance from the roadway. As such, there is often a need to protect the occupants of errant vehicles through energy absorbing infrastructure, such as road safety barriers. Another benefit of these devices is to protect errant vehicles from one another.

## Slide 10: Design that supports harm elimination
Reduce crash energy by reducing speed
Reduce impact angles
Forgiving roadside hazards
Eliminate potential for rollovers
Source: Centre for Automotive Safety Research
Source: Centre for Automotive Safety Research
Press enter to continue
Notes: Rollovers are often the unconsidered part of lane departures. While vehicle occupants can be protected from collisions with hazardous objects by removing these objects, this does nothing to protect from the risk of a rollover. Even relatively smooth, level roadsides can induce a rollover as vehicle snag on soft ground and unseen hazards such as spoon drains. Few infrastructure solutions are available for eliminating rollovers. The most promising are roadside barriers that are able to capture errant vehicles and slow them down progressively, rather than redirecting them or themselves inducing a rollover.

## Slide 11
Harm elimination examples
Notes: Next, we’ll look at two examples of harm elimination in practice, and how these examples differ from common practices that will not achieve the elimination of fatal and serious injuries.

## Slide 12: Harm elimination at intersections
High speed intersections pose a substantial risk to harm
Roundabouts support safer speeds and reduced impact angles
Source: Regional Roads Victoria
Source: Regional Roads Victoria
Press enter to continue
Notes: Intersections pose some of the greatest locations of risk for road users. Crashes at intersections often occur at high speeds and at crash angles that limit a vehicle’s ability to protect their occupants. Intersection along rural roads present a particularly high risk due to the high speeds at which these road are operated. Many intersection designs are reliant on reducing the potential for errors to be made. They however do nothing to limit the severity of crashes when they occur.
Roundabouts have been used in limited numbers since the early days of motoring. It is more recently that we have realised the safety benefits of roundabouts. Appropriately designed, roundabouts can limit vehicle speeds and impact angles to the point where severe injury outcomes are all but impossible. This is achieved because the design of roundabouts ensures all vehicles entering the intersection do so at a speed that is appropriate for the type of interactions that can occur.

## Slide 13: Harm elimination from head-on crashes
Head-on crashes contribute greatly to harm on rural roads
Wide centrelines can reduce crash likelihood
Median barriers reduce crash severity and remove the risk of head-ons
Source: Centre for Automotive Safety Research
Source: Dept. of Planning, Transport and Infrastructure
Source: Dept. of Planning, Transport and Infrastructure
Press enter to continue
Notes: Head-on crashes are a common cause of fatal and serious injuries along rural roads. The risk of head-on crashes is particularly high along undivided roads where there is very little space separating vehicles that are travelling in opposing directions. The relative speed of head-on crashes, particularly along high speed roads, ensures the high risk of severe injury outcomes.
The provision of more space between passing vehicles can help to reduce harm by reducing the likelihood that head-on crashes will occur. If a driver drifts out of their lane and towards the oncoming lane, a wide centreline provides them with more time to correct their vehicle’s path of travel before a head-on crash can occur. Working in this way, the wide centreline reduces the likelihood that a head-on crash will occur. However, a proportion of errant vehicles will still traverse into the oncoming lane. For these cases, any resulting head-on crash will generally be as severe with the wide centreline, as it would have been without the wide centreline.
However, if we implement a road safety barrier into the wide centreline, errant vehicles are now captured by the barrier and the possibility of head-on crashes is practically eliminated. Now, lane departures can occur and vehicles can cross the road centreline, but the barrier prevents these events from resulting in head-on crashes. While a crash with the barrier may occur, these crashes are likely to be far less severe than a crash with an oncoming vehicle. Hence, the harm that corresponds to head-on crashes is substantially reduced and may even be eliminated.

## Slide 14
Identifying Safe System design
Notes: Finally, let’s look at the core concepts of safe road design, and how to identify design and operation that will bring us closer to achieving a Safe System.

## Slide 15: Design that supports harm elimination
Are all points of exposure necessary?
Eliminate or reduce exposure
Exposure in space and time
Exposure
Likelihood
Severity
Press enter to continue
Notes: Exposure can often be overlooked in the design and operation of roads, as the decisions that affect exposure can be made at very early stages in their development. It is important that one of the first questions being ask is whether road users need to be exposed. Does a new intersection need to exist or can traffic be diverted to another, higher quality intersection? Do cyclists need to use a roadway or can they be diverted to a bicycle path? Do heavy vehicles need to access an area or are their alternative ways or times when goods can be delivered? These are just some of the questions that can be asked.
Eliminating points of exposure is the best way to ensure safe outcomes. Often though, full elimination of exposure is not possible. The next best alternative is to eliminate as much exposure as possible. This could mean removing a proportion of the possible conflict locations, or reducing the volume of traffic using a road. The remaining exposure can then be dealt with through reduction in the likelihood and severity of crashes.
Remember, exposure can occur in time as well as in space. A great example of exposure in time occurs around shopping centres. While alternatives to large heavy vehicle deliveries should be explored, another option could be to reschedule deliveries for times when pedestrians are not active around the shopping centre. Another example is the common practice of undertaking roadworks at night, when traffic volumes are low.

## Slide 16: Design that supports harm elimination
Does design/operation consider human vulnerability?
Design/operation best aligned with Safe System objectives will:
  Focus on reducing severity should a crash occur
  Not just rely on reducing crash likelihood
Likelihood
Severity
Exposure
Press enter to continue
Notes: Design and operation needs to consider human vulnerability. Whenever there is a risk that crashes can occur, we need to be mindful of the crash outcomes and ensure they are survivable for those involved. And remember, more vulnerable members of society, such as young children and the elderly, will be even more susceptible to harm in the event of a crash.
Considering human vulnerability means we need to think about more than just the likelihood of crashes. We also need to consider the outcomes when a crash occurs. This means considering the possible severity of a crash. Solutions best aligned to Safe System principles will deal with the severity of crashes, as well as their likelihood.

## Slide 17: Design that supports harm elimination
Is speed managed where conflicts between vehicles or with hazardous objects can occur?
As a rule of thumb
  30 km/h or less where vulnerable road users are not protected
  50 km/h or less where right angle are possible
  70 km/h or less where head on crashes can occur
Severity
Exposure
Likelihood
Press enter to continue
Notes: Speed is one of the most important factors in determining the risk of harm. While in certain situations speed in not the dominant factor, such as crashes between heavy vehicles and pedestrians, speed is generally a very good determinant of injury outcome. This means that managing speed is a critical component to a safe road transportation system. Generally, there are two ways to achieve appropriate speed: speed management through road design and operation, and vehicle technology; and speed compliance through speed limits and enforcement. Both ways have their place in a Safe System.
While numerous studies have looked at the relationship between fatal and serous injury risk and speed, there is currently no definitive answer to what speeds are safe. As a rule of thumb, the following speeds should not be exceeded: 30 km/h where vulnerable road user are not protected from motor vehicles; 50 km/h where right angle crashes between motor vehicles are possible; and 70 km/h where head-on crashes can occur. Remember, these speeds are a general guide and do not take into account all circumstances. Some circumstances, such as for motorcycles and interactions between vulnerable road users and heavy vehicles do not have an easy safe speed answer.