## Slide 1
Eliminating harm at intersections
Notes: Welcome to Module 3, Snippet 2 of Safe System for Universities. In this snippet, we will be talking about the harm of intersection crashes and the interventions available to eliminate harm at intersections.

## Slide 2
1.0
01 Jul 2020
Press enter to continue

## Slide 3: About this snippet
This snippet is made up of a number of sections. Click on the below links to go through each section. To advance a slide, press enter on your keyboard or click the slide.
Go to How does harm occur?
Start here
Go to Harm elimination mechanisms
Go to Primary treatments
Go to Supporting treatments
Notes: This snippet is made up of a number of sections. Click on the below links to go through each section. To advance a slide, press enter on your keyboard or click the slide. If you miss anything that has been said, you can replay the narration to each slide. A printed version of the narrative is also provided in the curriculum guideline.

## Slide 4
How does harm occur?
Module 3, Snippet 2
Notes: Firstly, let’s take a look at the mechanisms of harm associated with intersection crashes.

## Slide 5: Where does harm occur?
Source: Centre for Automotive Safety Research/Google Maps
Source: Centre for Automotive Safety Research/Google Maps
Module 3, Snippet 2
Press enter to continue
Notes: In the image on the left, we can see a map of right angle injury crashes that occurred between 2009 and 2018, in the inner southern suburbs of Adelaide, South Australia. In an urban environment such as this, signalised intersections tend to dominate the locations of intersection crashes. Despite the greater level of control and reduced likelihood of crashes at signalised intersections, the very high volumes of traffic using these intersections mean that they tend to experience more crashes than at intersections with lower levels of exposure. Unsignalised intersections along arterial roads also tend to experience a large number of crashes. This is due to the high exposure along arterial roads combined with the lack of control for traffic entering from side roads.
Like urban intersection crashes, rural intersection crashes tend to occur more at intersections with high volumes of traffic. Unlike in urban areas, rural intersection crashes are spread out over a vast area, with often much lower levels of exposure, meaning the random nature of these crashes can be more easily appreciated. In the image on the right, we can see a map of right angle injury crashes that have occurred over an area of nearly 3,000 square kilometres between Clare and Crystal Brook in South Australia. Due to the relatively high levels of exposure, most crashes have occurred in and around the townships, while those crashes occurring at intersections along the higher speed roads are less frequent but often more severe, due to the very high energy nature of these crashes.

## Slide 6: Mechanisms of harm
Traffic volume
Level of control
Arterial and distributor roads in urban areas
Townships and along higher trafficked roads
Source: Centre for Automotive Safety Research
Source: Centre for Automotive Safety Research
Press enter to continue
Notes: Generally, the risk of crashes occurring at an intersection are dictated by two factors – exposure, or the volume of traffic using the intersection, and likelihood, which is closely tied to the level of control maintained over road users traversing the intersection.
In urban areas, this means that the greatest number of crashes tend to occur at intersections with arterial and distributor roads that carry the vast majority of traffic. While signalised intersections maintain a high level of control, their placement at the highest volume intersections where arterial and distributor roads meet one another means a large number of crashes occur at these locations. Another frequent location of crashes is at the intersections of arterial or distributor roads and the local streets that join them – despite lower volumes of traffic entering the main traffic streams, a lack of control at these locations increases the risk that crashes will occur.
In rural areas, crashes tend to congregate around highly trafficked areas such as near and within townships. Crashes outside of these areas tend to be less frequent, but often much more serious due to the high speed nature of the roads along which they occur.
Poor intersection design, such as confusing intersection layouts, confusion regarding who is required to give way, poor visibility along intersecting roads or poor visibility of the intersection from the approach, can also contribute to a higher risk of crashes.

## Slide 7: Mechanisms of harm
Source: Centre for Automotive Safety Research
Source: Centre for Automotive Safety Research
Source: Centre for Automotive Safety Research
Uncontrolled
Controlled
Signalised
Press enter to continue
Notes: Generally speaking, there are three levels of control used to operate intersections. At minor T-junction intersections, no control can be employed. These are termed as uncontrolled intersections and require road users to revert to the road rules to understand who gives way to who.
The next level of control is by the use of regulatory control – which means using either stop and give way control. These intersections, termed as controlled intersections, define which roads are required to give way, and which are not. However, they still leave it to the road users to judge the situation and decide when it is safe to proceed through the intersection – a task that is often prone to error.
The greatest level of control, known as signalisation, is afforded to only the highest volume intersections. Termed signalised intersections, they are most commonly seen at the intersection of arterial and distributor roads. Generally, crashes occur at intersection when a road user, either purposely or through error, runs a red light, or with movements that are not fully controlled. At signalised intersections where filter right turns operate, which require right turning drivers to judge gaps in oncoming traffic, around half of all injury crashes can be associated with this movement.

## Slide 8: Mechanisms of harm
Right angle collisions
Lack of energy management
Little energy absorption by vehicle
Press enter to continue
Notes: Despite the level of control that may be employed, crashes are possible and when they do occur, the design of the intersection largely dictates the level of harm that can occur.
Most intersections occur at right angles. While good for visibility and improving the likelihood that a driver will see another vehicle approaching from the intersecting road, right angle collisions can be severe, due to the relative lack of protection afforded by a vehicle’s design. Unlike front and rear impacts, the side of a vehicle has very little room to absorb the energy of an impact before the occupant compartment is compromised.
Appropriate speed management is also lacking at many intersections, with vehicle speeds similar to those obtained between intersections, where the risk of a right angle collision is much lower. Speed management at intersections is generally limited to observation of the posted speed limit, or control from the minor road approach, where a vehicle may be required to stop or slow down and give way before entering the intersection. There is usually opportunity for vehicles on at least one of the approaches to traverse the intersection at speed.
The potential for high speed collisions at right angle orientations mean that kinetic energy levels of a crash can be well in excess of the human biomechanical tolerance to harm. As mentioned, the relative lack of protection afforded by a vehicle when collided with on its side means that considerable potential exists for this energy to be transferred to the vehicle occupants.

## Slide 9: Mechanisms of harm
Mass inequality
Heavy vehicles
Vulnerable road users
Source: Centre for Automotive Safety Research
Source: Centre for Automotive Safety Research
Press enter to continue
Notes: In addition to the roles of speed and impact angle, the difference in mass between colliding vehicles, known as the mass inequality, can play a substantial role in the outcomes of a crash. When a heavier vehicle collides with a lighter vehicle, the mass inequality means that the lighter vehicle will undergo greater acceleration, increasing force on the vehicle and in turn increasing the chance of severe injury outcomes to its occupants.
The issue of mass inequality is most recognisable with heavy vehicles. When a light vehicle collides with a heavy vehicle, the effect that the difference in the vehicle’s mass has on the crash outcomes are obvious. The lighter vehicle will undergo much greater deformation than if it collided with a vehicle of similar mass. In addition to the greater force felt by its occupants, the occupant compartment can be compromised to a much greater extent, increasing the risk of crushing injuries.
As well as with heavy vehicles, mass inequality can greatly disadvantage vulnerable road users, which are generally much lighter than the vehicle with which they collide. The much greater force felt by a cyclist, pedestrian or motorcyclist in a crash with a light vehicle compounds the effects of the lack of protective structure.

## Slide 10
Harm elimination mechanisms
Notes: Now, knowing how harm can occur at intersections, let’s take a look at what mechanisms are available for eliminating this harm.

## Slide 11: Harm elimination mechanisms
Historical focus on reducing likelihood
Now focus on likelihood and consequence
Eliminating exposure
Source: Centre for Automotive Safety Research
Source: Centre for Automotive Safety Research
Source: Department of Planning, Transport and Infrastructure
Press enter to continue
Notes: Reducing the likelihood of a crash is often a primary consideration of many intersection designs. Most engineering features implemented at intersections are focussed on improving the level of control, increasing guidance and conspicuity, and reducing the possibility of confusion and error. This focus on likelihood has served us well, with many intersections providing efficient mobility to high volumes of road users. However, as it attested in crash history Australia wide, errors still occur and these errors sometimes lead to severe injury outcomes. And as such, a focus on likelihood alone will not achieve zero harm.
When a crash does occur, the best chance to avoid a severe injury outcome is to reduce the kinetic energy of the collision to below the threshold of the human body’s biomechanical tolerance to harm. In practice, this means reducing speed and impact angles to the level where the kinetic energy imparted upon vehicle occupants involved in the crash is not enough to cause harm. To do this, the design of intersections needs to be reimagined to one where both likelihood and consequence are a part of the design brief, instead of likelihood alone.
There is also a third part to the equation – exposure is a key mechanism of harm and therefore can also be used to our advantage. Some movements, such as right turns and through movements, are more prone to high severity outcomes than others. Banning certain movements and redirecting traffic to safer intersections can also be a powerful tool in the effort to eliminate harm. The example you can see here was implemented along Greenhill Road, a centrally located arterial road in Adelaide. The works focussed in preventing right turns from intersecting local roads, instead redirecting traffic to U-turn facilities that reduced exposure to right angle conflicts.

## Slide 12
Primary treatments
Notes: Next, let us discuss the primary treatments – those best aligned to the Safe System objective of eliminating fatal and serious injuries.

## Slide 13: Grade separation
Eliminates exposure to cross-traffic
Large cost and space requirements
Generally reserved for high-speed environments
Source: Centre for Automotive Safety Research
Source: iStock.com (zetter)
Press enter to continue
Notes: Grade separation is one of the best options we have for eliminating harm at intersections, as it largely eliminates the intersection of traffic streams by allowing them to cross over or under one-another. The only points of collision that remain are where traffic enters or exits the traffic streams through slip lanes. When an intersection is grade separated, right angle and right turn crashes, which often represent the majority of harm at intersections, are eliminated as the associated movements no longer exist. Rear end crashes, which can contribute to harm, are also greatly reduced as there is no longer a need for traffic to slow or stop before traversing the intersecting traffic stream.
Grade separation involves a substantial amount of work and generally more land than an at-grade intersection. The costs associated with the physical construction work and the acquisition of land, especially at already constricted locations such as in urban areas, means that their use is limited.
The large financial costs involved in grade separating intersections, as well as their expansive footprints mean that they are generally reserved for use along high-speed, high-volume restricted access roads, such as freeways and expressways. Partial grade separation is used to a limited extent in urban environments, where major arterial roads cross one-another – the benefits of such partial grade separation are not as great as with full grade separation, as right turns are generally still required and dealt with through signalisation.

## Slide 14: Roundabouts
Generally best-performing at grade solution
Manages speed and impact angle
Safety benefits heavily affected by design
Press enter to continue
Notes: Roundabouts have been used for many decades, though their safety benefits have only more recently been understood. They represent one of the best at-grade solutions that we currently possess.
The geometric design of roundabouts means that all vehicles are required to slow down before proceeding through the intersection, ensuring the kinetic energy of a crash will be far lower than at traditional right angle intersections. Additionally, the reduced impact angle between vehicles at locations of conflict mean that the relative velocity and therefore acceleration and force undergone during a crash will also be reduced.
The safety benefits of roundabouts are due in a large part to their ability to manage speed through their design. This means that the design of a roundabout can greatly affect its ability to reduce or eliminate harm. Larger roundabouts, especially along multi-lane roads, are often less capable of achieving safe intersection speeds between vehicles. Access requirements for larger vehicles, such as trucks and buses, can also compromise the ability to reduce light vehicle speeds, though design details such as roll-over aprons can help avoid such tradeoffs.

## Slide 15: Roundabouts
Source: This Photo by Unknown Author is licensed under CC BY-SA
Can be compatible with signalisation
Several innovative design solutions
Compact rural roundabout
Source: This Photo by Unknown Author is licensed under CC BY-NC
Source: Regional Roads Victoria
Press enter to continue
Notes: In some circumstances, roundabouts can have reduced capacity compared to signalised intersections. More recently, large capacity signalised roundabouts have been used to combine the capacity benefits of a signalised intersection with the safety benefits of a roundabout. Signalised roundabouts work by coordinating vehicle movements onto or around the circulating area of the roundabout. Partial signalisation has also been used on roundabouts where unequal flows and tidal flows on commuter routes can cause delays to traffic on the lower-volume approaches.
Over recent years, a number of other innovative roundabout designs have appeared. Mini roundabouts have become popular in Europe and some applications have been seen in Australia. The small footprints of mini roundabouts, which can be no larger than that of a traditional intersection, make them an attractive solution at small local road intersections. Larger designs such as the hamburger or cut-through roundabout, the flower roundabout and the turbo roundabout are largely designed to improve the capacity of multilane roundabouts. Turbo roundabouts, such as the one shown here also have a demonstrated safety benefit over traditional multilane roundabouts.
Another innovative solution is the compact rural roundabout. Rural roundabouts, placed at the intersection of high speed rural roads, have been designed with very large circulating radii to handle the generally high speed of vehicles approaching the intersections. This in-turn has limited their usefulness at sites with constricted space. The compact roundabout uses vertical deflection on approach to the roundabout to better manage approach speeds, and a smaller circulating radii requiring less space than a traditional design. This makes the compact rural roundabout a promising solution at sites where traditional roundabout designs would have been rejected due to their large size.

## Slide 16: Raised safety platforms
Vertical deflection through intersection
Risk reduction through speed management
Progressively being used on arterial roads
Source: Regional Roads Victoria (top and bottom)
Source: Safe System Solutions
Source: Safe System Solutions
Press enter to continue
Notes: Raised safety platforms are a recent innovation on a relatively old form of traffic management – the speed hump. Like the speed hump, raised safety platforms rely on vertical deflection to slow vehicles as they traverse the treatment. Unlike speed humps, raised safety platforms have been developed with intersection applications in mind.
Raised safety platforms reduce risk by reducing vehicle speeds at the location of the treatment. When applied at intersections, they can reduce the speeds of all vehicles as they traverse the intersection. The speed reducing properties of raised safety platforms are dependent on their design, meaning vehicle speeds can be managed to desirable levels dependent on the application.
A variation on the raised safety platform concept is the raised intersection, where the entire intersection forms a raised platform. While raised safety platforms are successfully used on low volume, low speed roads, they have also been developed with higher speed, higher volume road applications in mind. So far, several raised safety platform solutions have been applied along arterial roads in Australia.
An example is the intersection of the Surf Coast Highway and Kidman Avenue in Belmont, Victoria. The speed limit along the Surf Coast Highway is 70 km/h, while the raised safety platform slows vehicles through the intersection to a safer 50 km/h.

## Slide 17
Supporting treatments
Notes: Next, we will discuss some of the supporting treatments available to practitioners.

## Slide 18: Reduced speeds
Reduce speed limit on approach to intersection
Enforcement may be an issue
Limited impact if not reinforced by road design
Source: Centre for Automotive Safety Research
Source: Centre for Automotive Safety Research
Press enter to continue
Notes: While roundabouts and raised safety platforms aim to reduce speeds to survivable levels, any reduction in speed through intersections is beneficial for reducing both the likelihood and severity of crashes. Reducing speed limits is an inexpensive means for reducing speed. While adherence to reduced speed limits, especially over short distances such as through intersections, can be an issue, it is important to remember that speed reduction, and not speed limit adherence, is the primary concern when prioritising harm reduction.
An issue with this approach is, however, the inability to ensure lower speeds are adhered to. Compliance to reduced speed limits over such short lengths of roadway and at regular intervals could be difficult to achieve. Speed enforcement, such as the use of speed cameras, may not be possible due to the close proximity of camera and speed limit signage locations.
Though tempting due to its low cost, speed limit reductions alone are likely to be only moderately successful at best. Better results may be obtained by road design that reinforces the lower speed environment. Such road design may also be successful in isolation.

## Slide 19: Full signalisation
Reduces likelihood of conflicts
Remove uncontrol right turns
Compatible with speed management treatments
Source: Centre for Automotive Safety Research
Source: Centre for Automotive Safety Research
Press enter to continue
Notes: Full signalisation, including the full-time control of right turns, can substantially reduce the likelihood of crashes at an intersection as uncontrolled turning movements commonly represent a high proportion of injury crashes at intersections where they are employed.
Uncontrolled right turn movements are especially hazardous at signalised intersections where they are employed. They require a driver to judge gaps within oncoming traffic, commonly comprising two or more oncoming lanes. Uncontrolled right turns are particularly hazardous for pedestrians and cyclists, as drivers making uncontrolled right turns may be focussed on judging gaps within oncoming vehicular traffic, rather than looking for these vulnerable road users.
While full signalisation can benefit a reduced likelihood in crashes, in isolation, signalisation does not deal with the consequence of crashes as speed is not managed in consideration with the types of interactions to which road users are exposed. Another complicating factor is that signalisation is commonly applied to high exposure intersections and intersections where rising demand dictates its need, thereby increasing exposure and therefore the risk of crashes. While signalisation alone will not achieve Safe System outcomes, combining signalisation with speed reducing treatments, such as raised safety platforms, may achieve near Safe System levels of performance.

## Slide 20: Restricting movements
Remove high-consequence movements
Left-in/left-out
Simplify intersection
Source: Centre for Automotive Safety Research
Source: based on Department of Planning, Transport and Infrastructure
Press enter to continue
Notes: Another way to reduce harm at intersections is to remove exposure to the more severe types of conflicts.
An example well-aligned to Safe System objectives is the left-in, left-out intersection, where all cross-road and right turn movements are redirected to U-turn facilities on the major road. While crashes are still possible through the left turn and U-turn movements, their severities are likely to be less severe than that of a right angle or right turn crash.
An added benefit of this type of treatment is the simplification of the intersection. Less movements are possible, meaning the driver’s task is simplified and errors are less likely to be made. Such simplification may also provide additional ability to safely deal with pedestrians and cyclists.

## Slide 21: Improved signage
Improves advanced warning, awareness of control
Vehicle operated signs
Intersection activated warning signs
Source: Centre for Automotive Safety Research
Source: Department of Planning, Transport and Infrastructure
Press enter to continue
Notes: Though not well aligned to a system’s perspective of road safety, improved signage can nevertheless help reduce harm by reducing the likelihood of error by road users. Improving signage can be particularly effective at locations where signage is below acceptable standards, or where there is a known, related safety issue.
More recently, technological innovations have led to electronic signage that can be activated by a vehicle’s presence. This brings the benefit of only displaying a warning or message when it is needed and can be related to an observable risk, so that its effectiveness is better retained.
One example is the rural intersection activated warning sign. When triggered by a vehicle exiting from a side road, the sign acts to provide warning or reduce the speed limit along the main road, with the aim of alerting passing vehicles and reducing their speed in the presence of the entering vehicle.

## Slide 22: Improved intersection conspicuity
Increased awareness of intersections
Channelisation and signage
Alternative designs
Source: Centre for Automotive Safety Research
Source: Department of Planning, Transport and Infrastructure
Press enter to continue
Notes: A proportion of crashes can be traced back to intersection or control conspicuity, where the driver was either unaware of the intersection or the need to give way to other traffic. A lack of intersection awareness is particularly problematic in rural areas, where infrastructure can be minimal.
A standard response is to increase and improve signage on the minor road approaches to the intersection. This may involve the installation of duplicate signage and advanced warning signs. Channelisation can also be used to improve intersection conspicuity by drawing attention to a change in the road environment.
The staggered T-junction design has been a standard response to improve rural intersection safety. Part of this design’s benefit is to highlight the intersection through termination of the minor roads. However, the use of staggered T-junctions has become unfavourable due to their high cost for minimal gain. Superior designs, such as roundabouts, can be implemented for similar cost.

## Slide 23: Turning lanes and channelisation
Reduced rear end conflicts
Reduced complexity of movements
Potential safety issues
Source: Centre for Automotive Safety Research
Source: Centre for Automotive Safety Research
Press enter to continue
Notes: Channelised and auxiliary turning lanes are often used to remove turning movements from through lanes and provide some separation from intersecting movements. This response can reduce rear end crashes when traffic waiting to turn does not queue back into the through lanes.
Such treatments may also simplify the driving task by separating and channelling individual tasks. For example, channelising uncontrolled right turns may reduce pressure to expedite the turn and therefore the risk of error by selecting inappropriately sized gaps in oncoming traffic.
Channelisation can also lead to potential safety issues. A prime example is the channelization of left turns at signalised intersections. Channelisation of the left turn can give an impression of priority for vehicle drivers, increasing the risk of conflict with crossing pedestrians.

## Slide 24: General intersection improvements
Street lighting
Skid resistance
Sight distance
Source: Centre for Automotive Safety Research
Source: Centre for Automotive Safety Research
Press enter to continue
Notes: Other general design improvements can benefit safety, especially where such design features are lacking. Adequate street lighting can improve the conspicuity of road users at night, reducing the risk that approaching drivers will miss detecting conflicts. Street lighting is especially important where pedestrians are expected, as they can be particularly difficult to see when dark.
Inadequate skid resistance can lead to serous safety issues, due to the increased braking distances that result. Improving already adequate skid resistance can help to improve safety, especially where there is a substantial risk of encountering conflicting movements at speed, such as along the major road approaches to intersections.
Sight distance is another design feature that may compromise safety when inadequately provided for. In addition to the regular consideration of static sight obstructions, such as vegetation and road furniture, consideration should also be given to dynamic visual obstructions. An example as shown here is dynamic visual obstruction from left turning vehicles on the major road, which can mask the presence of through vehicles from the perspective of a driver turning from the minor road.

## Slide 25: Enforcement and vehicle technology
Combined red light and speed cameras
Autonomous vehicle braking
Connected autonomous vehicles
Source: Centre for Automotive Safety Research
Source: Centre for Automotive Safety Research
Press enter to continue
Notes: A complete rethink of the way we design intersections is required if we are to achieve the elimination of death and serious injury on our road network. However, despite some promising solutions, we cannot achieve elimination through road design alone. Enforcement has presented some improvement in safety at intersections, especially at signalised intersections where the widespread use of combined red light and speed cameras had somewhat reduced intentional red light running and speeding.
Autonomous vehicle technology represents substantial possible gains in safety at intersections. Currently, autonomous braking technology is able to detect possible rear end collisions and reduce impact severity or completely avoid a crash. Upcoming technology should assist in avoiding other crash scenarios that are currently difficult to detect, such as right angle crashes.
Connected autonomous vehicles, or CAVs, are able to communicate with each other and smart infrastructure, such as connected traffic signals. While still some time from becoming mainstream, CAVs represent a promising solution to much of the harm that occurs at intersections. For example, CAVs technology may be able to completely avoid crashes resulting from red light running by stopping a vehicle before it traverses the red light.