## Slide 1
Eliminating harm from road departures
Notes: Welcome to Module 3, Snippet 3 of Safe System for Universities. In this snippet, we will be talking about harm due to lane departures and interventions for minimising this harm.

## Slide 2
1.0
01 Jul 2020
Press enter to continue

## Slide 3: About this snippet
This snippet is made up of a number of sections. Click on the below links to go through each section. To advance a slide, press enter on your keyboard or click the slide.
Go to How does harm occur?
Start here
Go to Barriers vs. clear zones
Go to Primary treatments
Go to Supporting treatments
Notes: This snippet is made up of a number of sections. Click on the below links to go through each section. To advance a slide, press enter on your keyboard or click the slide. If you miss anything that has been said, you can replay the narration to each slide. A printed version of the narrative is also provided in the curriculum guideline.

## Slide 4
How does harm occur?
Notes: Firstly, let’s take a look at how harm from lane departures occurs.

## Slide 5: Where does harm occur?
Source: Centre for Automotive Safety Research/Google Maps
Source: Centre for Automotive Safety Research/Google Maps
Press enter to continue
Notes: Road departure crashes are a substantial problem and one of the main contributors to harm on our roads. Road departures occur when a vehicles leaves its lane and collides with a vehicle in another lane, an object on the roadside, or rolls over as it departs the lane.
Fuelled by high speeds and long travel distances, road departures represent the majority of fatal and serious injury crashes in rural and remote areas. Exposure plays a large role in dictating where these crashes will occur, with many situated on arterial highways carrying the majority of traffic. Here, we see an about 15 km section of both the Horrocks and Barrier Highways north of Adelaide, in South Australia, which together serve both as important tourist and freight links. Here we can see a number of hit fixed object crashes, resulting in both hospitalisation, represented by the dots in red, and fatalities, represented by the dots in black, that occurred in the ten-year period from 2009 to 2018.
Often overlooked, road departure crashes also represent a substantial part of the harm problem in urban areas. The answers for mitigating harm caused by road departures in urban areas are often less clear than the answers for rural and remote areas. In the right image, we can see a map of hit fixed object crashes over a 10 square kilometre area of Adelaide’s inner western suburbs. Most of the injury crashes seen here have occurred on arterial and distributor roads, where speeds and traffic volumes are higher, with a mix of crashes at midblock and intersection locations.

## Slide 6: Mechanisms of harm
Lane departures into oncoming traffic
Lane departures into non-frangible roadside objects
Vehicle roll overs
Rear-end crashes (in urban areas)
Source: Centre for Automotive Safety Research
Source: Centre for Automotive Safety Research
Source: Centre for Automotive Safety Research
Press enter to continue
Notes: Most road departures end with little seriousness with respect to the outcomes. Either the driver of the vehicle is able to recover the errant vehicle or the vehicle stops before any obstacles or other vehicles are hit.
Harm occurs when a driver is unable recover the errant vehicle, or is unable to do so in time. The first mechanism for harm is a head-on collision with another vehicle. This occurs when an errant vehicle crosses paths with another vehicle travelling in another lane, coming in the opposing direction. This can occur even when the road is divided by a median. Head-on crashes can also occur when a vehicle is overtaking and is required to travel along the opposition direction lane to do so. The generally high severity of these crashes is due to the often very high relative speed of the colliding vehicles.
Harm can also occur when an errant vehicle leaves the road and strikes a roadside object. Non-frangible objects, those that for all intents and purposes do not move when struck, are the most likely to cause severe outcomes.
When a vehicle leaves the road, harm can occur even when an object is not struck. Roll overs occur when a vehicle “trips” and rolls onto its side or roof. A tripping mechanism can be anything from the road surface to a curb to uneven roadside ground. Vehicles with higher centres of gravity are more prone to rolling over. Heavy vehicles can even roll over without loosing control – the forces exerted on a heavy vehicle when cornering can be enough to cause it to tip.
Rear-end crashes, though not normally due to lane departures, are another mechanism for harm prevalent in urban areas. While most rear end crashes result in low severity outcomes, the sheer number of these crashes has led them to contribute meaningfully to the number of deaths and serious injuries on our roads.

## Slide 7: Lane departures
Drift-off scenario (potentially recoverable)
Yawing scenarios (not recoverable)
Prevalent on straights and horizontal curves
Woolley et al (2018)
Doecke & Woolley (2011)
Press enter to continue
Notes: The mechanisms for lane departures can differ between situations. In general, they either can occur as a drift-off, where the vehicle departs the lane in a controlled manner, or as a yaw, where the vehicle quickly becomes uncontrolled and acts largely free of the driver’s inputs.
The first scenario, a drift-off, occurs when the driver is in some way distracted and allows the vehicle to depart the lane. At this stage, the vehicle is still controllable but the driver is not using this control to keep the vehicle within its lane. Compared to a yaw, a drift-off scenario still provides scope for the driver to retain control and correct the vehicle’s path. Generally, successful regain of control will require progressive brake and steering inputs. If this is done before colliding with another object, such as a roadside hazard or another vehicle, a crash can be avoided.
The second scenario is a yaw. A yaw occurs when the driver has lost control of the vehicle and it begins to spin around its vertical axis. Yaw scenarios can result from unsuccessful recovery of a drift-off scenario or from an evasive manoeuvre, such as to avoid an animal on the roadway or another vehicle that has entered the vehicle’s lane. Yaw scenarios are generally not recoverable by a driver, but may be prevented by electronic stability control if fitted to the vehicle.
Both drift-off and yaw scenarios can result in either a head on crash with another vehicle or a run off road crash that results in a roll over or collision with a hazardous object. While the risk of a lane departure may seem more prevalent around horizontal curves, they are also likely to occur on straight sections of road, where a lack of concentration for only a few seconds can lead to a drift off scenario. It is important to remember that once a yaw occurs, a vehicle is likely to traverse the centre line of an undivided roadway, even if the final crash occurs on the left side of the road. This scenario is referred to as a double yaw and is a common mechanism for run off road crashes to the left side of the roadway.

## Slide 8: Run off road vs. head-on
Run off road crashes dominate low volume roads
Cross-centreline crashes a substantial issue
Most rural roads not designed to mitigate cross-centreline crashes
Source: NZTA (2011)
Press enter to continue
Notes: As we have discussed, lane departures can lead to either head on or run off road type crashes. Whether a lane departure results in a head on or run off road crash is dependent on whether a vehicle travelling in the opposing direction is present or not at the time of the loss of control. For this reason, the relative risk of either a head on or run off road outcome is highly dependent on the volume of traffic using the road. A New Zealand study found that while the rate of head on crashes per kilometre of roadway increased in a linear relationship with traffic volume, the rate of run off road crashes increased in a logarithmic relationship, so that the relative likelihood of a head on crash was greater once a threshold volume was reached.
The relationship between traffic volume and the rate of head on crashes means that they can become a substantial issue as traffic volume increases. The need for centreline protection is exacerbated by the fact that most run off road crashes involve a centreline incursion. All run off road to the right crashes involve a vehicle crossing the centreline, as do a substantial proportion of run off road to the left crashes. This is because a key mechanism for run off road to the left crashes is the double yaw, where a vehicle crossed the centreline before departing the roadway to the left.
Unfortunately, most rural roads in Australia and New Zealand are poorly designed to cope with crashes that involve a centreline incursion. At best, most roads involve some type of roadside barrier to help mitigate run off road impacts. In comparison, centreline protection would enable mitigation of almost all head on and run off road to the right crashes, as well as a substantial proportion of run off road to the left crashes. This is achieved by a centreline barrier that can capture a vehicle before it yaws off to the left and departs the roadway.

## Slide 9
Barriers vs. clear zones
Notes: Now that we understand the core mechanisms of lane departure crashes, let’s look at the two main ways of treatment, road safety barriers and clear zones.

## Slide 10: Clear zones
Obstacle-free space for errant vehicles to slow down and stop
In practice, rarely adequate in width or lack of obstacles
Poor ground preparation/maintenance can lead to vehicle roll-overs
Source: Centre for Automotive Safety Research
Source: Centre for Automotive Safety Research
Press enter to continue
Notes: Clear zones are flat areas of ground, free from obstacles, that flank the side of a roadway. They provide space for an errant vehicle to slow down and stop before colliding with any hazardous objects, thereby averting a potentially severe run off road crash and instead resulting in a loss of control incident from which a driver may potentially be able to drive away. In Australia and New Zealand, Austroads guidance recommends clear zone widths dependent on adjacent roadway’s design speed, traffic volume and the lateral slope of the clear zone.
In practice, clear zones rarely conform to ideal standards. In all but the best maintained motorway and arterial rural road environments, roadsides are often maintained well below the recommended clear zone standards. Common issues are reduced clear zone width, hazardous obstacles within the clear zone and low quality ground preparation. Maintaining these facilities to recommended levels can be prohibitively expensive and can require land acquisition and clearing intruding into adjacent private land or within the roadside vegetated roadside reserve that, in agricultural areas, can form a substantial part of the habitable environment for wild animals.
Poor ground quality can be a core issue with clear zones and may lead to high severity roll over crashes. Soft ground material, ruts and low lying obstacles such as drainage pits can all lead to tripping hazards that may result in a roll over. The quality of clear zone required to prevent a roll over can be underestimated and seemingly well maintained clear zones, such as the one pictured here, can initiate roll overs.

## Slide 11: Clear zones
Source: Austroads (2012)
Run off road casualties do not coverge to zero
Press enter to continue
Notes: Critically, recent evidence has shown that the severe crashes that are meant to be treated by clear zones are not completely eliminated, irrespective of how wide the clear zone is. While clear zones are effective at eliminating a proportion of these crashes, their effectiveness is subject to a diminishing rate of return to the point where adding to the width of substantially wide clear zones will have little affect on the rate of severe crashes.
In other words, there is a residual of run off road crashes that are not affected by clear zone width. This residual is enough to ensure that a substantial proportion of the lane departure problem will remain, even when clear zones designed beyond current recommendations are employed. For this reason, the most recent editions of Austroads Guides to Road Design and Road Safety rely less on the use of clear zones as a primary way to treat lane departure crashes on high speed rural roads.

## Slide 12: Clear zones
Source: Doecke & Woolley (2011)
Press enter to continue
Notes: A study performed in 2011 by the Centre for Automotive Safety Research at the University of Adelaide looked at the simulated outcomes of lane departures, based on real crashes that were investigated by the centre. The reconstruction of vehicle speed and movement was used to recreate conditions of the crash, which were then exposed to a scenario where the vehicle was able to slow to a stop without colliding with roadside objects. This process was used to estimate the lateral displacement of the vehicle from its initial travel lane.
The results of this study showed that vehicles regularly depart roads with enough speed to result in a severe outcome in the event of a collision with a roadside object, even when the vehicle has reached the extent of current clear zone widths. The findings of this study also suggest that clear zones would need to be unrealistically wide if serious crashes with roadside objects are to be eliminated.

## Slide 13: Barrier protection
Capture vehicles from lane departures before a more severe collision
Prevent collisions with more hazardous obstacles or other vehicles
Reduce the severity of crashes, rather than prevent them from occurring
Can result in more crashes of reduced severity
Source: Safe System Solutions
Source: Centre for Automotive Safety Research
Press enter to continue
Notes: Road safety barriers are becoming the primary treatment for harm caused by lane departures. They are in most situations considered as leading practice and, depending on their design, can achieve near Safe System levels of performance. The fundamental principle behind the operation of road safety barriers is to capture a lane departed vehicle before it collides with a more hazardous object.
Historical thinking led road safety barriers to be considered as hazards in their own right and therefore their use to be avoided unless necessary. Knowledge of their benefits has since moved forward to a point where road safety barriers are considered as preferential to the provision of clear zones. While a collision with a road safety barrier comes with the risk of injury, this risk is substantially lower than if the vehicle in question is allowed to continue its lane departure and roll over, or collide with a hazardous object or another vehicle.
While clear zones are idealistically meant to prevent crashes altogether, barriers do not prevent lane departure crashes but instead reduce their severity. This is achieved by capturing and controlling the departure of vehicles. Barriers can therefore be viewed as a liability, as they become a maintenance issue whenever they are struck. This is particularly true of flexible barriers, which require maintenance after even minor hits. However, another perspective on the maintenance issue is that every collision with a barrier is a potential severe injury crash that has been avoided.
The provision or road safety barriers can result in an increase in lane departure crashes, when compared to the use of clear zones. However, the benefit of road safety barriers is that these crashes are generally of a reduced severity. The result is a reduction in serious injury crashes, compared to where clear zones are employed.

## Slide 14: Types of barriers
More recent designs aimed at “capturing” vehicles and reducing impact severity
Type of barrier chosen is context-important
Issues with certain travel modes (e.g. motorcyclists)
Source: Centre for Automotive Safety Research
Source: Centre for Automotive Safety Research
Source: Centre for Automotive Safety Research
Higher severity
Moderate severity
Lower severity
Rigid barriers
Semi-rigid barriers
Flexible barriers
Press enter to continue
Notes: Road safety barrier performance, or their ability to reduce the severity of crashes, is largely dependent on their design. Road safety barriers are general split into three categories: rigid, semi-rigid and flexible barriers. Rigid barriers, generally made of concrete or steel, often result in the most severe outcomes. Semi-rigid barriers are able to deflect on collision and often result in less severe outcomes, due to the reduced acceleration on colliding vehicles. Most semi-rigid barriers in Australia and New Zealand are of a steel w-beam design. Flexible barriers provide the greatest level of deflection and therefore the lowest acceleration to colliding vehicles and their occupants, which often leads to the least severe outcomes. Wire rope safety barriers are the most common type of flexible barriers.
It is important to consider the context of application when selecting the desirable type of barrier. While flexible barriers are best for most applications where light vehicle crashes are concerned, they may not be appropriate for containing heavy vehicles and therefore the use of stronger, more rigid barrier designs may be required. The deflection of barriers also needs to be considered. Where hazardous objects are very close to the roadside, the use of more flexible barriers may still lead to a collision with the hazard behind the barrier.
Road safety barriers also present as substantial hazards some road user types. Motorcyclists, and to a lesser extend bicyclists, may be severely injured in a collision with a barrier. The common mechanisms of injury are collisions with the barrier’s support posts in a sliding position, and slicing and snagging from sharp points along the barrier when still mounted on the motorcycle or bicycle. W-beam barriers are substantially hazardous when the top edge of the barriers and support posts are left exposed, and the support posts are left unprotected.

## Slide 15: Historical best practice
Clear zones
Flat, limited slope
Wide separated dual carriageways
Spot hazard protection (barriers)
Source: Centre for Automotive Safety Research
Press enter to continue
Notes: As we have discussed, clear zones have historically been employed as a primary treatment.
Clear zone surfaces have idealistically been flat or with a limited slope, and obstacle-free. While high standards are able to be maintained along the highest priority roads, such as freeways and motorways, clear zones along many other roads have either been designed or maintained below Austroads guidelines.
Along dual carriageway roads, clear zones have also been employed to separate opposing direction lanes. Along many of these roads, median barriers are now being retrofitted as the performance issues of clear zone-based design has been acknowledged.
However, the use of road safety barriers has historically been reserved for spot treatment when hazardous obstacles and non-traversable roadsides were unable to be removed or corrected.

## Slide 16: Safe System best practice
Full length flexible barriers
Median and roadside
Wide, flat run out areas where barriers not feasible
Source: Centre for Automotive Safety Research
Press enter to continue
Notes: Today, the treatment of lane departure crashes is being aligned to Safe System principles by prioritising full length, flexible barrier installations over clear zones. Other less forgiving barrier types, such as semi-rigid and rigid barriers, are employed where flexibles barriers are not feasible, such as where large roadside drops are present or where barrier deflection cannot be safely contained.
In order to achieve near Safe System performance, flexible barriers are being employed along both the roadside and centreline for the full length of the roadway. This ensures that any vehicle departure will be captured by the barrier.
Counter to historical practice, well maintained, wide and flat run out areas are utilised only at locations where barrier installation is not feasible.

## Slide 17
Primary treatments
Notes: Now, we will take a look at barrier design in the context of a primary Safe System treatment.

## Slide 18: Safe cross sections
Standardised cross sections for safe rural roads and urban expressways/freeways
Selection dependent on role, volume and strategic importance of the road
Need to consider travel modes (e.g. containment of heavy vehicles)
Source: Centre for Automotive Safety Research
Source: Safe System Solutions
Source: Centre for Automotive Safety Research
Lower speed
Press enter to continue
Notes: An example of primary Safe System design is being standardised by Regional Roads Victoria to guide their high speed road design now and into the future. These standardised designs are based on the context of achieving a fatal and serious injury-free network by 2050, and are based on certain assumptions such as the safety performance of vehicles across the network in 2050. These designs have been created with the recognition that while Safe System performance will take time to achieve, we need to set a tangible target date if it is ever to be achieved.
Primary designs are context sensitive, and are based on assumptions of the role and strategic importance of roads now and into the future. Roads of greater importance, such as very high-volume roads and strategic freight routes may receive high levels of infrastructure funding. For roads of lesser importance, infrastructure funding is likely to be scarce and Safe System performance will need to be achieved in other ways.
Travel mode is an important consideration that may dictate changes to standardised design. For example, heavy vehicle routes may require altered barrier design to ensure heavy vehicles departures are contained. Achieving Safe System performance for other modes, such as motorcycles, may not be possible with current knowledge and may require alternative design as this knowledge improves.

## Slide 19: Safe cross sections
Possible for the highest priority roads
Based on employment of continuous, flexible barriers
Other supporting treatments may also be utilised
Source: Regional Roads Victoria/SSRIP
Press enter to continue
Notes: Transformative works that see route-level implementation of Safe System aligned infrastructure improvements will only be possible for a small proportion of the network. Along these roads, current extra-urban speed limit setting can be upheld to prioritise faster travel times for the high volumes of traffic using these roads. Currently, some strategically important roadways, including the expressways and freeways that carry traffic into and between urban centres and other important locations, are built to such standards.
A high level of design means that flexible barriers will be employed along both the roadside and median to contain all errant vehicles before more severe collisions can occur. Where flexible barriers are not permissible, other barrier types may be used. Hybrid installations, such as using rigid barriers behind flexible barriers to ensure heavy vehicle containment while still providing the most forgiving design for the majority light vehicle users, may also be employed.
One concept of such a roadway has been envisaged through Victoria’s development of a zero death and serious injury strategy. This concept calls for all high-speed multi-lane roadways to be continuously barrier lined, with sealed shoulders and breakdown lanes to reduce the likelihood of lane departures and provide for safe emergency stopping areas outside of travel lanes.

## Slide 20: Safe cross sections
Undivided highways and high volume/arterial roads
Roadside and centreline barriers
Adequately sized sealed shoulders
Regular passing lanes
Source: Regional Roads Victoria/SSRIP
Press enter to continue
Notes: A high level of infrastructure design may also be possible along strategically important single-lane regional and rural arterial highways. Where an appropriate level of funding is available, infrastructure improvements can be used to ensure safe travel at high speeds in line with current extra-urban speed limit setting.
Along these roads, roadside and centreline road safety barriers are employed to contain all road departures. Like with higher order roads, flexible barriers are preferred but may be replaced by other barrier types in locations where they are not suitable.
To facilitate passing without placing road users at risk of head-on collisions, passing lanes need to be provided at regular intervals. An example of this concept in practice can be seen with Sweden’s “two plus one” roads, along which passing lanes are continuously provided along alternating directions of the roadway. Regular but not continuous passing lanes may be used where such a high level of provision is not feasible.

## Slide 21: Safe cross sections
Other undivided rural roads
Reliance on speed management
Targeted infrastructure treatments
Higher speeds possible as infrastructure and vehicle technology improves
Source: Regional Roads Victoria/SSRIP
?
Press enter to continue
Notes: While the scale of transformation required is immense, the scale of road network is even larger and so we will inevitably face the question of in which roads we will choose to invest. Where high levels of financial investment are justified, such as for reasons of traffic volumes, strategic importance of a road, community value or the needs of specific road users, transformative works will be undertaken. For the rest of the network, we must find an alternative solution to providing safe mobility.
For the vast majority of our rural and remote road network, this will mean a reliance on speed management through lower speed limits, enforcement and infrastructure improvements at high risk locations, such as the use of targeted barrier installations. Currently, there remains a large gap between current rural and remote road speeds, and what is safe given the infrastructure and vehicle technologies at our disposal. Public and political attitudes to lowering speed limits, especially where travel distances are great, often mean that speed limit reductions are unpalatable.
However, in the near future, as targeted infrastructure investment continues and vehicle technology improves, achieving safe speeds will become increasingly possible. As an example, through its development of a zero death and serious injury strategy, Victoria has estimated that, by the year 2050, speeds of up to 80 km/h will be safe where head on collisions between passenger vehicles are possible.

## Slide 22: A Safe System approach
Speed down
Design up
Safe mobility
Source: Safe System Solutions
Source: Centre for Automotive Safety Research
Trade-off between expenditure and mobility
Press enter to continue
Current conflict between safety and mobility
Notes: Whatever specific design approach is taken, a socially and politically driven conflict between safety and mobility is likely to endure. Envisioning what constitutes a safe road design is ultimately much easier than finding a solution that satisfies both the desired safety and mobility capacities set by our society.
One avenue for settling this conflict is to employ a practice of safe mobility. This means that mobility becomes a function of safety to ensure that safe road access is always provided. The conflict then becomes one between mobility and financial expenditure.
On high order road where financial outlay can be justified, transformative infrastructure works can be used to maintain safe mobility at higher speeds, such as those in-line with current extra-urban speed limit setting. On low order roads where traffic volumes are limited and costly infrastructure improvements are unable to be funded, speed management must be used to provide safe mobility. This ultimately means lowering speed limits and managing new speed limits in-line with what is survivable in environments where lane departure crashes are permissible.
The most difficult decisions will likely be those along high volume but lower priority routes that do not form a key part of the network strategy. The hard decision of whether to design up in order to allow higher speeds, or reduce speed to ensure safe mobility without extensive infrastructure investment, then becomes a question of social priority where a choice must be made between improving mobility or redirecting funding to other more critical social investments.

## Slide 23: A zero KPI
Section of strategic route from Melbourne to eastern Victoria
Step-change in harm elimination
Mass implementation of barriers
Source: VicRoads (bottom and right)
Longwarry, Vic.
Traralgon, Vic.
Press enter to continue
Notes: An example implementation of Safe System aligned roadway design comes in the form of the infrastructure improvements rolled out along a section of the Princes Highway between Longwarry and Traralgon in eastern Victoria. In this case, a transformative approach was taken to secure Safe System performance with regard to lane departure risk while maintaining the mobility expected of such a strategically important roadway.
The works implemented along this route constitute a step change towards harm elimination. Rather than focussing on only the highest risk locations of the route, the entire road environment was transformed to bring safety performance up to Safe System levels.
At the core of this approach was the mass installation of full length roadside and median barriers. Flexible barriers were prioritised and other barriers types where utilised only where flexible barriers were not permissible.

## Slide 24: A zero KPI
Source: VicRoads
SSRIP 1
SSRIP 2
SSRIP 3
SSRIP 4
TZAP
Step-change (transformation)
Press enter to continue
Notes: Starting in the early 2000, full-length road safety barrier investment was prioritised along the route under the Safe System Road Infrastructure Program, or SSRIP. The progress of barrier installation was modest until funding was attained through the Towards Zero Action Plan in 2017. By 2019, road safety barrier installation should be completed along the vast majority of the route.
In combination with vehicle safety technology improvements and ongoing speed management, it is projected that this section of roadway will be free of fatality and serious injuries by the year 2050 or before.

## Slide 25
Supporting treatments
Notes: While full length barrier installation and speed management constitute the primary approach to achieving Safe System performance, other treatments are available that, while not achieving harm elimination alone, can support the journey towards this goal.

## Slide 26: Supporting treatments
Sealed shoulders with edge line audio tactile line marking (ATLM)
Wide centrelines and centreline ATLM
High quality, well maintained run off areas
Source: Regional Roads Victoria
Source: Centre for Automotive Safety Research
Source: Safe System Solutions
Press enter to continue
Notes: Sealed shoulders are one of the most commonly used lane departure treatments across Australian and New Zealand roads. Sealed shoulders provide drivers with room to recover from some lane departures and can therefore reduce the likelihood of lane departure crashes. They are especially effective when combined with driver warning mechanisms such audio tactile line marking.
Centreline audio tactile line markings are another regularly used treatment for reducing the likelihood of lane departures across the centreline of an undivided roadway. These can be combined with wide centrelines to further reduce crash likelihood. Like sealed shoulders, wide centrelines increase the amount of space that a driver has to recover from a lane departure before venturing into the path of obstacles, which in this case are oncoming vehicles. An additional benefit of wide centrelines is that they provide space for centreline barriers to be retrofitted at a later stage.
Where barriers cannot be employed, high quality, well maintained run off areas reduce the likelihood that lane departures will result in severe outcomes through rolling over or collisions with hazardous objects. Such run out areas also allow sufficient space for barriers to be installed at a later stage.

## Slide 27: Supporting treatments
High standards of design (e.g. improved skid resistance, superelevation, gentle roadside slopes)
Consistent delineation and signage
Consistent design along routes (e.g. no out of context curves)
Technological solutions (e.g. vehicle activated signage)
Source: Centre for Automotive Safety Research
Source: Centre for Automotive Safety Research
Press enter to continue
Notes: There are many other treatments that can help reduce the risk of crashes. It is important to remember that most of these work on reducing likelihood but do not affect the consequences of crashes when they occur. Most good road design practices will to some extent benefit road safety, but will not lead to the elimination of fatal and serious injuries. Good road design is about achieving at least a minimum standard across the entire network and treating sub-standard locations that pose a heightened risk to those traversing their locations. However, to achieve Safe System performance, we will need to look past these historical practices as the only form of intervention.
Beyond conventional practices, a number of technologically-based solutions are coming to market and may prove to be viable supporting treatments. Vehicle activated signs are becoming more prevalent as a cost-efficient treatment at high-risk locations such as rural intersections and out of context curves on high speed roads. One such device first implemented in New Zealand and known as the rural intersection active warning system, or RIAWS, is activated by side road traffic and warns drivers along the main road that a vehicle is about to enter the roadway. A modified version reduces the speed limit along the main road when side road traffic triggers the system. This technology is being trialled in Victoria and South Australia, and has shown promising results for reducing vehicle speeds through intersections when side road traffic is present.

## Slide 28: Other considerations
Speed enforcement
Delineation, signage and overall design compatible with autonomous vehicle technology
Consideration of human needs (e.g. rest areas to mitigate fatigue)
Source: Centre for Automotive Safety Research
Source: Centre for Automotive Safety Research
Press enter to continue
Notes: Considerations outside of the infrastructure realm offer varying degrees of promise for reducing the harm that is being created on our roads. Speed enforcement is likely to remain a key tool for maintaining safe mobility. The role of speed enforcement will need to be carefully considered as it will not alone solve the problem. Speed enforcement is likely to be of greatest benefit where it can help maintain speeds within a reasonable envelope and reinforce the setting of speed limits. A key improvement to speed enforcement could be the use of mobile point-to-point speed cameras, which may help fill the gap of enforcement along lower order regional and rural roads.
Autonomous vehicle technology is fast gaining pace. A key limitation of autonomous vehicles is looking to be the road environment along which they are travelling. Autonomous technology requires consistent and easy to read road environments to be effective. A key challenge for road system managers will be to implement and maintain delineation, signage and overall road environment design that is compatible with autonomous vehicles.
A key part of the Safe System is acknowledging the limitations of humans and designing a road transportation system that considers these limitations. Further consideration of human needs and limitations will play a part in a Safe System. As well as design that is accepting of human error, which play a core role of Safe System-aligned design, is design that helps to reduce human error. An example of this type of design is regularly spaced rest areas along long distance rural routes to help alleviate the effects of driver fatigue.