## Slide 1
Safe System design tools
Notes: Welcome to Module 3, Snippet 6 of Safe System for Universities. In this snippet, we will be looking at the range of tools available to assist road designers in achieving Safe System levels of performance.

## Slide 2
1.0
01 Jul 2020
Press enter to continue

## Slide 3: About this snippet
This snippet is made up of a number of sections. Click on the below links to go through each section. To advance a slide, press enter on your keyboard or click the slide.
Go to What are Safe System tools?
Start here
Go to Road assessment programs
Go to Crash modification factors
Go to Safe System assessments
Go to KEMM-X
Notes: This snippet is made up of a number of sections. Click on the below links to go through each section. To advance a slide, press enter on your keyboard or click the slide. If you miss anything that has been said, you can replay the narration to each slide. A printed version of the narrative is also provided in the curriculum guideline.

## Slide 4
What are Safe System tools?
Notes: Firstly, let’s take a look at what tools are available to assess alignment with the principle of eliminating fatal and serious injuries.

## Slide 5: Types of road safety tools
Reactive approach
Based on crash data
Vulnerable to crash variability
Can only be applied to existing roads
Proactive approach
Based on road and traffic attributes
Independent of statistical variation
Applicable to new and existing roads
Press enter to continue
Notes: Generally speaking, there are two types of tools employed in identifying and evaluating the safety of road design and operations: reactive and proactive tools. Historically, reactive tools have been employed as a mechanism for gaining road safety funding, such as through the Black Spot programs. More recently, proactive tools are being considered as a potentially better way to prioritise funding, though the mechanisms for sourcing such funding are still limited.
Reactive tools are based on crash data. While reactive tools provide a direct measurement of harm, they rely on harm having already occurred before it can be identified and treated. This means they can only be applied retrospectively, preventing their use on new or substantially altered roads.
On the other hand, proactive tools rely on the direct identification of road and traffic attributes to predict future harm. A benefit of this is that proactive tools can be applied before the road is even constructed and harm has had a chance to occur. However, proactive tools can be limited by their reliance on indirect measures, which may not always be a reliable indicator of future harm.

## Slide 6: Reactive tools
Press enter to continue
Notes: A notable issue with the reactive approach is a reliance on crash clustering to highlight problem hotspots, such as blackspots. While this approach has achieved considerable success over the past decades, severe crash numbers have decreased with continued treatment of blackspots, to a point where most severe crashes are occurring in locations with little or no recent crash history. As a result, reactive approaches are achieving diminishing returns with crash locations that are now largely scattered across the road network and not easily reducible to individual problematic locations. This is a particular issue on local government and other low volume roads, where exposure to crash risk is limited and crashes occur infrequently enough to make patterns in the data almost impossible to detect.

## Slide 7: Proactive tools
Press enter to continue
Notes: Proactive approaches are, on the other hand, better equipped to deal with the scattered existence of crashes across the network. Their focus on systematic problems allows for the identification of locations not necessarily associated with a recent crash history. This also makes them applicable to new as well as existing parts of the road network, allowing problems to be identified even at pre-construction stages, before crashes have had a chance to occur. While both proactive and reactive tools have their benefits and drawbacks, proactive tools are seen as more closely aligned to Safe System principles, as they do not rely on waiting form harm to occur before enabling system managers to act upon the risk of harm.

## Slide 8: Tools aligned to harm elimination
Proactive approach
Energy management
Focus on road and traffic attributes
Source: VicRoads
Source: Centre for Automotive Safety Research
Press enter to continue
Notes: As we have discussed, most tools well aligned to Safe System principles are proactive in nature: they focus directly on identifying risk through known relationships with road and traffic attributes, instead of a retrospective reliance on harm that has already occurred.
At the core of most proactive approaches is their focus, in one form or another, on energy management. In other words, the approaches often allow for the identification and prioritisation of design and operational conditions that reduce the release of high kinetic energy onto road users, which is associated with severe crash outcomes.
Their general focus on road and traffic attributes can also allow some of these approaches to identify design and operational details that need to be remediated in order to reduce the risk of harm. For example, the identification of high-risk movements at an intersection, the benefits of conversion to roundabout control, or the need to separate oncoming traffic along high speed roads.

## Slide 9: Level of application
Source: based on Woolley et al (2018)
Strategy
Program
Network
Route
Project
Design
Strategic review
Road Assessment Programs
(RAPs)
Crash reduction factors
Safe System Assessment Framework
KEMM-X
Press enter to continue
Notes: A number of tools well-aligned to Safe System principles are available for a range of applications, from strategic prioritisation of works to detailed design changes affecting elements of individual projects.
Strategic reviews are aimed at high level oversight and administration. While often not targeted only to road safety, their use can help alignment to the Safe System through strategies and procedures that prioritise safety outcomes and set defined performance criteria.
Road assessment programs aim to quantify safety performance of a road based on its physical and operational features. They are widely applicable from strategic prioritisation of road treatments and upgrades to route and project level assessments.
Crash reduction factors provide information about the safety performance of specific treatments and programs. Their generic nature means they are more applicable to larger scale works than individual design elements, where situational details may magnify inaccuracies. It is worth noting that crash reduction factors still rely on crash histories as they are generally based on crash studies.
The Safe System Assessment Framework is a recently developed tool useful for qualifying Safe System alignment of individual roads and road elements based on assessment with a focus on infrastructure. The scalability of the Safe System Assessment Framework means it can be applied to route, project and detailed design levels.
At the detailed design level, models such as the kinetic energy management model are useful for assessing the severe injury risk of different impact configurations and speeds. For example, when applied to intersections, such a tool is useful for identifying risk associated with geometric design details of the intersection, such as intersecting road angles, speed management devices and channelization.

## Slide 10
Road assessment programs
Notes: Now that we’ve taken an overview of the types of tools available, let’s discuss some examples. Firstly, we’ll take a look at road assessment programs.

## Slide 11: Road assessment programs (RAPs)
Similar in theory to the new car assessment programs (NCAPs)
Undertaken internationally (iRAP) and by several countries worldwide
In Australia, known as AusRAP
Similar national programs operate in countries such as Brazil, Thailand and South Africa
Source: This Photo by Unknown Author is licensed under CC BY-SA
Source: This Photo by Unknown Author is licensed under CC BY-NC-ND
AusRAP
KiwiRAP
ChinaRAP
IndiaRAP
usRAP
EuroRAP
Press enter to continue
Notes: Road assessment programs, or RAPs, provide an easy to understand measure of the level of risk on our road network. Like the new car assessment programs that put stars onto cars to provide a quick and easy measure of a vehicle’s safety rating, road assessment programs put stars onto roads so that industry professionals and the public alike can better understand the safety ratings of the roads that they are using. RAPs are especially useful for road authorities, as they provide an easy to access forum for identifying risk on the road network.
Road assessment programs are undertaken in several countries around the world, with some falling under the international road assessment program organisation. In Australia and New Zealand, our programs are known respectively as AusRAP and KiwiRAP.

## Slide 12: Road assessment programs (RAPs)
Risk mapping based on many factors
  Speed
  Road design
  Roadside environment
  Exposure
Provides risk scores and a star rating scheme
Source: adapted from AusRAP (2016)
Source: adapted from AusRAP (2016)
 Low risk

 Moderate risk

 High risk
Press enter to continue
Notes: Road assessment programs score the safety risk of a road through a series of factors. Once evaluated, the scoring can be graphically presented on maps that show how the safety risk changes over the length of the road network. Some of the factors evaluated as part of the risk scoring including traffic speed and the speed limit, the geometric design of the road, the roadside environment including the provision of barriers, and exposure levels such as traffic volumes. Data for these factors is collected through a variety of means, including road surveys conducted by a specially equipped vehicle that traverses the length of the road network that is being assessed.
From the scoring system, a star rating is developed for each section of road to signify the broad level of safety risk. Star ratings range from one star, signifying a high risk of harm, to five stars, which signifies a low risk of harm. Each additional star represents a halving in the risk of fatal and serious injuries. Star ratings can be developed for both personal risk, which is the risk to each person traversing the roadway, or collective risk, which is analogous to the frequency of expected harm.

## Slide 13
Crash modification factors
Notes: At a level of detail greater than the road assessment programs sits crash modification factors, which detail the level of benefit supported by each type of treatment.

## Slide 14: Crash modification factors (CMFs)
Similar to crash reduction factors (CRFs)
Based on empirical data analyses
Provide generic crash rate reductions for various treatments
-45%
-70%
Press enter to continue
Notes: Crash modification factors provide a quantitative estimate of the safety effect of a road safety treatment. They are generally aimed towards infrastructure treatments and are used to estimate the reduction or increase in harm that a treatment will produce. Crash modification factors, and the similar crash reduction factors, are based on empirical data analysis. Empirical studies from a sample of each treatment type are used to create a estimate of the general effect size of the treatment, which then becomes the crash modification factor. Crash modification factors may estimate the effect size on all crashes, injury crashes, or severe injury crashes.
As an example of a crash modification factor, converting an unsignalized intersection to signalisation may affect the likelihood of right turn and adjacent direction crashes. Crash modification factors can be used to estimate the effect on these crash types. In this example, two crash modification factors are involved and they each provide an estimate of the reduction in their respective crash types. Crash modification factors for various crash types are available in the Austroads Guide to Road Safety. A key limitation of crash modification factors is their generalisation of effect sizes that may be substantially effected by local factors, such as the local road environment, the traffic environment and they specific design of each treatment.

## Slide 15
Safe System assessments
Notes: Safe System assessments are a recent development that aim to provide a Safe System perspective on the concept of road safety audits.

## Slide 16: Safe System assessments
Scalable and applicable to all stages of project development and deployment
Scores alignment to harm elimination potential
Provides treatment hierarchy with a focus on road infrastructure
Primary
Supporting
Other
Severity
x
Likelihood
x
Exposure
Risk
=
Press enter to continue
Notes: Like road safety audits, Safe System assessments aim to provide a qualitative appraisal of safety for specific locations within the road network. Safe System assessments however aim to bring a Safe System perspective to the assessment process, by considering the potential for harm elimination. Safe System assessments can be used to assess a range of project scopes, from single intersections to entire routes. They can also be employed at different stages of a project, from concept development to implementation and ongoing operations.
Safe System assessments provide a qualitative assessment of the harm elimination potential supported by the road design and operation. Like road safety audits, they are meant to provide more than just a check against the standards and guidelines used to design and operate roads. Instead, they are about highlighting the harm potential from the perspective of all road users by estimating risk associated with the exposure to crashes, the likelihood of crashes, and the consequences once a crash occurs. While they can be implemented at any stage during the life of a project, their benefits are generally greater when implemented at the earlier stages when more than just detailed design changes are still possible.
Safe System assessments were first formalised through the Austroads Safe System Assessment Framework research report, published in 2016. In this report, a broad categorisation of treatments is provided to help guide practitioners to use those treatments that are better aligned to Safe System outcomes. These treatments are categorised by their alignment to the Safe System. Safe System or primary treatments are those that promise near harm-elimination performance. Supporting treatments, which reduce harm but will not eliminate it, are separated into those that are compatible with the future implementation of Safe System treatments, and those that do not affect such future implementation. Other considerations lying within the speed, vehicle technology and road user behaviour pillars of the Safe System are also provided.

## Slide 17: Safe System assessments
Consider two design options for a new rural arterial highway…
Option 1: wide footprint with grass median and clear zones
Option 2: narrow footprint using median and roadside barriers
Source: Safe System Solutions
Source: Centre for Automotive Safety Research
 | Run off road | Head on | Intersection | Other | Pedestrian | Cyclist | Motorcyclist
Exposure |  |  |  |  |  |  | 
Likelihood |  |  |  |  |  |  | 
Severity |  |  |  |  |  |  | 
Product |  |  |  |  |  |  | 
4
4
4
4
0
1
3
1
1
4
2
3
3
2
4
4
4
2
4
4
4
16
16
64
16
0
12
24
 | Run off road | Head on | Intersection | Other | Pedestrian | Cyclist | Motorcyclist
Exposure |  |  |  |  |  |  | 
Likelihood |  |  |  |  |  |  | 
Severity |  |  |  |  |  |  | 
Product |  |  |  |  |  |  | 
4
4
4
4
0
1
3
3
2
4
2
3
3
2
4
4
4
2
4
4
4
48
32
64
16
0
12
24
Press enter to continue
Notes: As an example application of the Safe System assessment, we can consider two design options proposed for the design of a rural multi-lane arterial highway. The first option incorporates a more historical design, with a wide footprint consisting of a dual carriageway separated by a grass median and lined by clear zones. The second option incorporates Safe System principles by utilising median and roadside barriers to contain any road departures that may occur.
Scores ranging from zero to four are applied to each of seven typical crash types and each of the three risk influencers. A higher score indicates a higher risk for that particular crash type and risk influencer.
The product of the risk influencers for each crash type are calculated to give the total risk of harm for each crash type. The total risk score can be calculated as the sum of all the crash type risk scores. As can be seen here, Option 1 produces particularly high scores for run off road, head on and intersection type crashes, owing to high traffic volumes and the high severity of crashes when they occur.
Option 2 can be scored in the same way, providing a platform for directly comparing the risk generated by the competing options. It is important to remember that risk scoring is subjective, as each Safe System assessor may score each risk differently. This limitation can be mitigated by ensuring that comparative assessments are undertaken by the same assessor and that justification is given throughout the process as to the scores awarded for each category.

## Slide 18: Safe System assessments
Source: Centre for Automotive Safety Research (top), Safe System Solutions (bottom)
Chart: 
| Run off road | Head on | Intersection | Other | Pedestrian | Cyclist | Motorcyclist
Option 1: wide footprint | 48 | 32 | 64 | 16 | 0 | 12 | 24
Option 2: narrow footprint | 16 | 16 | 64 | 16 | 0 | 12 | 24
Sum = 196
Sum = 148
Press enter to continue
Notes: We can now see, side-by-side, the level of risk generated by each option. Option 2, which utilises road safety barriers over the more historical clear zones, offers a reduced risk of harm due to the reduction in crash severity that these barriers afford.
The Safe System assessment provides a way to compare each design and pinpoint where the respective risk originates. For this example, we can see that the reduction in overall risk is actually due to a reduced risk of run off road and head on crashes.
More than this, Safe System assessments allow us to see where a residual of risk resides. In this example, we can see that although the use of road safety barriers reduces the risk of lane departure type crashes, they do nothing to improve the risk of harm at intersections. In this way, we can see where a risk of harm still exists and therefore where further attention needs to be paid.

## Slide 19
KEMM-X
Notes: We will finish this snippet by looking at Kemm X, which represents one of several risk models that can be used to inform detailed design.

## Slide 20: Kinetic energy management model (KEMM)
Conceptual model of transfer of energy in a crash
Human vulnerability at centre of model
Made up by five layers of protection
  Human biomechanical tolerance to harm
  Transfer of kinetic energy to human
  Kinetic energy of crash
  Crash risk per exposure
  Exposure to potential crashes
Source: based on Corben et al (2010)
Press enter to continue
Notes: Kemm, which stands for the kinetic energy management model, is a conceptual model of the pathway to harm from crashes on our road network. In this way, it forms a model of the potential to be affected by the energy of a crash and the transfer of energy when a crash occurs.
At the centre of the model is the human vulnerability to harm. Radiating out from this are the barriers that exist along the pathway to harm, which can either protect a human from harm, or in the case of gaps within the barriers, lead to the occurrence of harm.
There are five layers to the Kemm model. From the centre of the model outwards are the human biomechanical tolerance to harm, which is the human bodies ability to withstand physical impacts; The transfer of kinetic energy of the crash to the human body; the kinetic energy of the crash event; the risk of a crash event per exposure; and the exposure to potential crash events

## Slide 21: KEMM for intersections (KEMM-X)
Applies KEMM model to intersection
Energy transfer modelled as a product of speed and impact angle
Powerful tool for intersection design
Source: based on Jurewicz et al (2017)
U1
U2
Press enter to continue
Notes: Kemm X is a version of the Kemm model that has been specifically developed for understanding the risk of harm at intersections. A key part of Kemm X is the risk of severe crash outcomes given the travel speeds of the vehicles involved in the crash.
In Kemm X, this risk is modelled on the impact speeds and impact angles of two colliding vehicles. Using this model, we can determine for two vehicles, U1 the bullet vehicle and U2 the target vehicle, what is the proportional likelihood of having severe injury outcomes as a result of a crash.
Kemm X is a powerful tool that can be employed by intersection designers to test the potential for harm to occur with different designs. By using this tool, system managers can select the most appropriate type of intersection and designers can detail the specific design of an intersection while being fully informed about the risks associated with each option. Tools like this provide system managers with the evidence required to make informed choices and to select the best possible outcomes for road users.