## Slide 1
Breaking the barriers to implementation
Notes: Welcome to Module 4, Snippet 5 of Safe System for Universities. In this final snippet, we will discuss three key factors critical to the implementation of the Safe System. Sometimes viewed as barriers, these factors in fact hold the key to unlocking Safe System practice in the real world.

## Slide 2
0.1
Draft not for release
Press enter to continue

## Slide 3: About this snippet
This snippet is made up of a number of sections. Click on the below links to go through each section. To advance a slide, press enter on your keyboard or click the slide.
Go to The response to harm
Start here
Go to The role of standards and guidelines
Go to The design domain
Go to Moving forward
Notes: This snippet is made up of a number of sections. Click on the below links to go through each section. To advance a slide, press enter on your keyboard or click the slide. If you miss anything that has been said, you can replay the narration to each slide. A printed version of the narrative is also provided in the curriculum guideline.

## Slide 4
The response to harm
Notes: Our response to harm drives the way we manage safety within the road transportation system. Generally, our response to harm involves two key factors: the ethical responsibility and legal liability of system managers. Now, we will discuss these two factors and how they can contribute to a good or poor response when harm occurs.

## Slide 5: A response to harm
Decisions made by a system manager
Press enter to continue
Harm occurs to a system user
Ethical response
Can reoccurrence of harm be prevented?
Liability response
Are our decisions reasonably defendable?
Notes: Ethical responsibility and legal liability are two concerning factors that should weigh into any decisions made by system managers. These two factors play a critical role into both day-to-day functions and the responses made when something goes wrong. The ethical responsibility of a system manager is generally concerned with ensuring the safety of the people who use and work within the road transportation system. On the other hand, legal liability is concerned with ensuring that system managers are taking all reasonable precautions to minimise the risk of loss or harm that could burden a system stakeholder. When loss or harm does occur, legal liability is about a reasonable level of defence for the decisions made by system managers.
When harm occurs on the road network, our response is critical to preventing more harm from reoccurring in the future. A well-reasoned response will consider both the ethical responsibility and legal liability of system management. A good response will help to protect the system managers who made sound decisions, as well as prevent harm from further occurring in the future.
A good response will involve a review of the safety conditions that led to the harm occurring in the first place. This should be more than just a review of the standards and guidelines, and will ideally involve a thorough investigation of all the factors that led to the crash and subsequent harm, such as through the processes outlined in the Austroads Guide to Road Safety. The aim here is to minimise the risk that harm will reoccur, especially when the mechanisms of that harm can be reasonably identified and countermeasures exist to mitigate the risk.
The second part of a good response is to review the legal liability of the road authority and the decision makers who manage the road network where the harm occurred. The best response is a proactive response. This means ensuring that system managers have a reasonable level of defence for their decisions, should something go wrong and someone is harmed. One way of achieving this is by considering the standards and guidelines that spell out how the road system should be designed and managed, and the design domain under which those decisions are made. We’ll talk more about standards, guidelines and the design domain later on. For now, you can think about a good legal liability response as one that considers the reasonable level of defence for the decisions made by a system manager, given the financial, capacity and capability constraints under which they operate.

## Slide 6: Risk management
Design the road
Risk management (minimising net risk)
Harm occurs
Review practices to minimise risk
Legal and ethical response
Update practices
`
`
`
`
`
Press enter to continue
`
Legal liability response
Review practices to meet minimum standards
`
Business as usual
`
`
Notes: Now let’s look at the response to harm through the lens of risk management. We want to design the road to minimise the net risk of harm. While we would ideally like to eliminate the risk of any harm, it is well known that system managers work within constraints that mean this is not always possible. These constraints could be the limited availability of funds, meaning we have limited capacity to ensure safety. They could also be constraints of knowledge, meaning we do not always have the data and understanding required for perfect judgement. Simply put, we prioritise and make decisions to minimise the overall risk to road users, while working within the constraints that are laid upon us.
We design and build roads while trying to minimise harm. But in doing so, we also know that we are creating a system in which some people will be harmed. However, we do not always understand exactly where or how this harm will manifest itself. Therefore, when harm does occur, we must use the knowledge gained through these events to address the deficiencies that led to harm occurring in the first place.
A reasonable response will consider both the system managers’ ethical responsibility to minimise harm, as well as their legal liability with regard to the decisions that they make. In the context of risk management, this means we must respond in a way that reduces the risk to road users, through both identifying and mitigating existing risks, and ensuring that we have and will continue to work within the limits of our capability and knowledge.
A poor response, on the other hand, will view risk only from the perspective of liability towards the road authority and the system managers who act within it. Such a response can lead to practice that aims to ensure only the minimum required standards are met. As outlined within the Austroads Guide to Road Design, a road designed to meet the minimum standards is not necessarily safe.
A response to harm should ultimately lead to a point where prior decisions and practices are critiqued and revisions are made to correct prior errors and oversights. A good response will view this in light of the trade-offs between design parameters that are inputted and the level of safety that results. When harm does occur, the question should be asked as to whether the design parameters were sufficient to reasonably minimise the risk of harm. In the context of risk management, this is analogous to the factor of safety that is used in other areas of engineering. In this sense, we need to ask ourselves whether the factor of safety was sufficiently great enough to ensure a harmful event does not occur.
On the other hand, a poor response will likely not question design beyond the scope of the minimum required standards. Such a response may cover a road authority and its system managers in the sense of their legal liability, but will ultimately fail to question whether the safety requirements of road users where reasonably addressed. In taking such an approach, we fail to consider our ethical responsibility towards road users by failing to use our sound engineering judgement to minimise risk within the constraints with which we work.
The result of a good response to harm should lead to recommendations for improving design practices, should insufficient practices be identified. A good response can also help identify factors outside of the design realm that may need to be rectified, with recommendations to improve practices both inside and outside of a road authority’s direct control. These recommendations can then be weighed up against the trade-offs that may result, such as the cost of rectifying insufficient design. Moreover, when system managers are informed of the risks posed by current practices, the defence for continuing these practices is reduced and change which further minimises the risk of harm is more likely to occur. In this sense, the added value of such a process is the ability to inform future design practices, so that similar risks can be identified and improved design practices can be implemented.
The results of a poor response are, on the other hand, less likely to inform better design practices in the future. Instead, business as usual will continue to occur and the same mistakes that led to harm in the first place are more likely to be repeated.

## Slide 7
The role of standards and guidelines
Notes: In the previous section, we mentioned standards and guidelines, and their role in a reasonable response to harm. Standards and guidelines form a basis for the minimum level of design that should be attained. However, they can sometimes be viewed as an instruction manual that outlines the level of performance to which a road should be designed. The difference between these two ideas is subtle but important. Next, we will discuss the role of standards and guidelines in the context of minimising harm.

## Slide 8: Bounding safety outcomes
Standards and guidelines
Poor safety outcomes
Leading safety outcomes
Press enter to continue
Notes: Standards and guidelines have been created as safety nets that set a minimum acceptable level of performance. In this sense, standards and guidelines ensure that design and operational practices below minimum accepted limits do not enter the road transportation system. In practice, this removes much of the possible risk to road users and is a substantial reason why we today do not see considerably more death and serious injury on our roads.
However, the purpose for which standards and guidelines have been created is not the same as the way they are sometimes put into practice. A response to standards and guidelines may be to treat them as a benchmark for good design, instead of a safety net to mitigate the risk of sub-standard design. Such a response is counter to the idea that designing to minimum standards does not guarantee safe outcomes. The risk here is that the minimum standards of design become the only values that we adopt. The context of design and the relationship to risk are both forgotten. In other words, we set out to achieve the minimum level of performance, without considering what the minimum level of performance entails.

## Slide 9: Bounding safety outcomes
Standards and guidelines as safety net
Poor safety outcomes
Leading safety outcomes
Design needs to be sensitive to a Safe System context
Press enter to continue
Notes: A leading idea within the current design fraternity is that of context sensitive design. Context sensitive design is about recognising the environment in which a road will operate. This allows a designer to create solutions while recognising the trade-offs and limitations with which the design must contend. A key consideration of context sensitive design is the need to adopt design that is in keeping with the Safe System approach. In this sense, context sensitive design needs to incorporate consideration of how to make a road safe, rather than just how to make a road safer within the confines of the current standards and guidelines.
As stated by the United States Federal Highway Administration and outlined within the Austroads Guide to Road Design, context sensitive design asks questions about the needs of transportation. In the context of the Safe System, this means asking questions about providing safe transportation. In this sense, we can use context sensitive design as a way to pursue Safe System outcomes by better understanding how design can be sensitive to the needs of providing safe mobility. In the following section, we will pursue this idea in the context of the design domain, an concept of road design that is closely aligned to the idea of context sensitive design.

## Slide 10
The design domain
Notes: We finished the last section by introducing the design domain. Next, we will discuss the concept of the design domain, its relationship to context sensitive design, and how this may be used to pursue safe road design within the context of a Safe System.

## Slide 11: The design domain
Source: based on Veith et al (2006) and McTiernan et al (2019)
Traffic Volume
Range of values (e.g. safety performance)
Extended Design Domain
Normal Design Domain
Increased risk of liability
Press enter to continue
New and innovative practices
Decreasing scope for defence
Increasing survivability
Notes: The design domain may be viewed as the tangible boundary in which context sensitive design can be practiced. It is the bounding area under which accepted levels of practice are situated. In the real world, the design domain forms the set of design and operational practices that lead to a certain level of performance. The concept of a road design domain in Australia was developed several decades ago. This concept was based around the idea of context-sensitive, cost-effective design that considers the performance limitations of drivers and their vehicles. As such, much of the design domain is focussed on the geometric design of rural and high speed roads, such as through setting standard lane widths and curve geometry based on assumptions of vehicle performance. The normal design domain as shown here is the performance standard to which we design when building new roads or upgrade existing roads. The lower bound of the normal design domain constitutes the current minimum acceptable level of performance for these situations.
Next to the normal design domain sits the extended design domain. This is essentially an area of diminished performance. It is our acknowledgement that previously built and currently operated parts of the road network will not always perform to the same level to which new roads are designed. As you may have noticed, traffic volume plays a part in deciding where the boundary of the domain lies, as higher traffic volumes mean it is harder to justify a low level of performance due to the greater number of people that are exposed to the design. As such, the minimum level of acceptable performance increases with the traffic volume.
Legal liability and a scope for defence are two concepts that we have previously discussed. In short, they represent the ability for system managers to defend their decisions on the grounds of sound engineering judgement. In the context of the design domain, the selection of design values below the bounds of the design domain increases the scope for legal liability, should something go wrong and a road user is harmed. In other words, the scope for defending one’s decisions are decreased. In this context, it is possible to view any design above the bounds of the design domain as appropriate, given that design within the design domain can form a defence for one’s decisions.
As outlined within the Guide to Road Design, there is a potential for collisions to occur on any road, and so designing a road to a set of standards does not necessarily guarantee safety. Improving survivability on our roads beyond the capability of current practice can mean the need to look to new and innovative ideas. However, such practices can lie outside of the current design domain, because they are often too new or innovative to yet reside within the standards and guidelines that have been agreed upon as the scope for normal design practice. This means that we can potentially discourage design that brings us closer to the elimination of harm, purely because it sits outside of our current idea of normal practice.

## Slide 12: Safe System design
Exposure
Survivability
Current design domain
Safe System design*
Transition to survivable
Decreasing survivability
Innovative energy management -based system design
*A System Design approach that integrates vehicle technology, road design and speed in a transformation context
Sub-standard design
Press enter to continue
Notes: In this light, we can ask the question as to whether the current concept of a design domain is adequate? Should there be a Safe System design domain in which design and operational practices move closer and closer to achieving a safe road transportation system where all crashes are survivable? It is important to note that such a domain does not currently ensure survivability and will not achieve survivability within the confines of infrastructure improvements alone. Instead, a Safe System design domain, applied within a transformation context, sets us towards the goal of zero deaths and serious injuries within a foreseeable timeframe by utilising capabilities from all pillars of the Safe System.
A Safe System domain lies within the context of more than just infrastructure. A systems-based approach is needed that integrates infrastructure decision making within the context of vehicle technology, speed, and other elements. The backbone of such a systems-based approach is the design and operational practices that manage energy within the road transportation system to survivable levels.
By looking at safety performance from this perspective of survivability, we can question whether our current design practices can produce survivable outcomes and therefore whether these practices are acceptable in the context of a Safe System. Where practices under the current design domain are unable to guarantee survivability, we will need to look beyond the current accepted norms and to the proposed Safe System design domain, with practices that are increasingly able to produce survivable outcomes. Additionally, while the design domain as it currently stands can incorporate Safe System aspects of design, the effect of vehicle technology and speed on energy management need to be included together with geometric design considerations to provide a system response, rather than one built specifically on one aspect of road transportation.

## Slide 13: A transformative design domain
Exposure
Survivability
Normal design domain*
Transition to survivable
Decreasing survivability
*A System Design approach that integrates vehicle technology, road design and speed in a transformation context
Sub-standard design
Innovative energy management -based system design
Press enter to continue
Notes: Ultimately, transformation would see a future where the proposed Safe System design domain becomes the normal design domain, and anything below this qualifies as sub-standard to accepted minimum levels of safety performance. In other words, design and operational practices that are based on energy management and ensure survivability become the minimum accepted level of performance. Achieving this will require a complete rethink of the standards and guidelines to which we currently design and operate the system.

## Slide 14: The normal design domain
 Standardises minimum practice
 Primarily likelihood based
 Primarily consequence based
 Deals with energy and crash consequence
 Hierarchy based on Safe System alignment





Source: Centre for Automotive Safety Research
Source: iStock.com (greenantphoto)
Press enter to continue
Notes: As an example, let’s look at the way intersection control is dealt with in the current Austroads guidelines, and how this could differ in a Safe System design domain. Currently, the Austroads Guide to Road Design promotes the use of both signalisation and roundabouts as way to control traffic at intersections. Guidance for both types of control falls within the normal design domain, based on standardised design informed by a range of factors including safety and mobility.
Where the current guidelines fall short is in discerning the priority of use based on safety criteria. The use of both signalisation and roundabouts are justified on safety grounds, but there is little guidance to discern safety performance in the context of energy management and alignment with Safe System objectives. While this type of information is available in other Austroads publications, such as their research report on improving Safe System performance at intersections, guidance within the standards and guidelines utilised by designers may take years to manifest and has the potential to be diluted by competing agendas, such as the need to maintain intersection throughput.

## Slide 15: Safe System design
 Standardises minimum practice
 Primarily likelihood based
 Primarily consequence based
 Deals with energy and crash consequence
 Hierarchy based on Safe System alignment





Source: Centre for Automotive Safety Research
Source: iStock.com (greenantphoto)
Press enter to continue
Notes: In a Safe System design domain, performance of design options would need to be clearly illustrated in the context of energy management and alignment to Safe System objectives. This would then feed into design hierarchies that promote the use of well-aligned design first, and give clear reasoning for when lesser design can and cannot be considered as alternatives. In a Safe System design domain, the safety superiority of certain design, such as roundabouts, and the potential for risk of harm associated with each form of design would be clearly outlined and used to govern guidance.

## Slide 16
Moving forward
Notes: Now that we have a better understanding of some of the barriers to achieving safe roads, let’s finish by summarising how the management of risk can help to inform a Safe System.

## Slide 17: Moving forward
Press enter to continue
Consideration of liability only
Consideration of ethical responsibility and liability
Designing to minimum standards
Designing to minimise harm
Meeting minimum accepted levels
Designing within a Safe System domain
Notes: In this snippet, we have discussed some of the key barriers to transformation. There are likely to be others, and these will become clear as we work closer towards dissolving the barriers of which we are already aware. For now, we need to progress beyond a tendency to design to minimum requirements. The design domain and context-sensitive design have helped move the industry away from this tendency. Going forward, we need to align these design practices with the design principles implied by the Safe System.
At the start of this snippet, we looked at the concept of ethics and liability, and how aiming to achieve risk minimisation, rather than conformation to minimum standards, can help to achieve a good response to harm on our road network. Ethical responsibility and liability go hand-in-hand. Going forward, we need to better define the ethical responsibility of road managers towards road users.
As we have discussed, there is a risk of treating standards and guidelines as design benchmarks, instead of the design safety nets for which purpose they were created. A response to harm that is predicated on liability alone is more likely to prioritise the achievement of minimum standards, rather than a level of design that minimises the risk of harm. We need to be mindful of this issue and instead base our response to harm on an ethical foundation, as well as a liability one. Doing so will lessen the risk that we base our design decisions on meeting minimum standards and instead design towards an agenda of minimising harm within the context of our current levels of understanding.
Finally, the design domain was created to shift the design goalposts beyond attaining only minimum acceptable levels of design. This is currently achieved through the notion of a context-sensitive approach to design. Going forward to a Safe System future, we will need to adopt leading-practice in safety as our benchmark for design. To do this, we need to establish design guidance that is not only context-sensitive, but also harm-sensitive. In other words, we need to adopt a design domain that is based on mitigating the mechanisms of harm.